## Slide 2: Commissioning function block IDENTControl IC-KP2-2HB21-2V1D
Standard TwinCAT 3 function block
with SingleFrame protocol
EtherCAT

## Slide 3: IC-KP2-2HB21 SingleFrame TwinCAT 3
This documentation is valid with the following specification:
Beckhoff PLC and TwinCAT 3 programming environment
Single frame protocol
Valid for the IP (125kHz) and IQ (13.56MHz) systems
Valid for the system IU (868MHz) with configuration protocol mode QV "SingleFrame"
IDENTControl IC-KP2-2HB21-2V1D (EtherCAT)

## Slide 4: IC-KP2-2HB21 SingleFrame TwinCAT 3
Content Download:
Version history
Documentation (DEU, ENG)

## Slide 5: IC-KP2-2HB21 SingleFrame TwinCAT 3
Content:
Scannen nach angeschlossenen Geräten
Verknüpfung Prozessdaten
Änderung EtherCAT Telegrammlänge
Firmware Version auslesen
Konfiguration Prozessdatenfelder
Ein- und Ausgänge Funktionsbaustein
Deklaration Funktions- und Datenbaustein
Aufbau Datenbaustein
Schematische Darstellung Bausteine
Beispiel 1: Initialisierung
Beispiel 2: Single Read Fixcode (UID) One-time read access to the Fixcode (UID)
Beispiel 3: Single Read Words One-time read access to the user memory
Beispiel 4: Single Write Words One-time write access to the user memory
Beispiel 5: Enhanced Read Fixcode (UID) Permanent read access to the Fixcode (UID)
Beispiel 6: Enhanced Read Words Permanent read access to the user memory
Beispiel 7: Enhanced Write Words Permanent write access to the user memory
Beispiel 8: Quit Canceling an Enhanced command
Beispiel 9: Single Read UII (EPC) One-time read access to the UII/EPC
Beispiel 10: Enhanced Read UII (EPC) Permanent read access to the UII/EPC
Beispiel 11: Single Program Special Fixcode (EPC) One-time write access to the UII/EPC
Beispiel 12: Single Write Fixcode (IPC11) One-time write access to the Fixcode
Beispiel 13: Enhanced Write Fixcode (IPC11) Permanent write access to the Fixcode
Beispiel 14: Special Command  Auslesen Sendeleistung Execution of freely definable command
Beispiel 15: Special Command  Einstellen Sendeleistung Execution of freely definable command

## Slide 6: IC-KP2-2HB21 SingleFrame TwinCAT 3
Scanning for connected devices:
Activation of Config Mode
Right-click on “Device 5 (EtherCAT)”  Scan  IDENTControl with the telegram length set in the device appears

## Slide 7: IC-KP2-2HB21 SingleFrame TwinCAT 3
Link process data field input data
Activation of Config Mode
Right-click on “IN_CH1”  Change link  Activate Array Mode  GVL_IDENTControl.BUS_INPUT[1]  Link from byte 0 to byte 63

## Slide 8: IC-KP2-2HB21 SingleFrame TwinCAT 3
Link process data field output data
Activation of Config Mode
Right-click on “OUT_CH1” Change link  Activate Array Mode  GVL_IDENTControl.BUS_OUTPUT[1]  Link from byte 0 to byte 63

## Slide 9: IC-KP2-2HB21 SingleFrame TwinCAT 3
Change EtherCAT telegram length
Activation of Config Mode  Scan to detect connected device  Double-click on the "IDENTControl Compact 64 Byte IN/OUT" module  EtherCAT  Advanced settings

## Slide 10: IC-KP2-2HB21 SingleFrame TwinCAT 3
Change EtherCAT telegram length
ESC access  EEPROM  Smart View  Write EEPROM  Select new module size

## Slide 11: IC-KP2-2HB21 SingleFrame TwinCAT 3
Change EtherCAT telegram length
Remove module  Scan  Module read in with new telegram length  Link process data

## Slide 12: IC-KP2-2HB21 SingleFrame TwinCAT 3
Read firmware version
Double-click on IDENTControl Compact module  CoE - Online

## Slide 13: IC-KP2-2HB21 SingleFrame TwinCAT 3
Configuration of process data fields
Definition as global variables (GVL)
BUS_OUTPUT = Output data field
BUS_INPUT = Input data field
Multidimensional array with a length of 254 bytes

## Slide 14: IC-KP2-2HB21 SingleFrame TwinCAT 3
Inputs and outputs function block:

## Slide 15: IC-KP2-2HB21 SingleFrame TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
pADR_IN | PVOID | Address Input data field
cbSIZE_IN | UDINT | Length Input data field
pADR_OUT | PVOID | Address Output data field
cbSIZE_OUT | UDINT | Length Output data field
I_T_Timeout | TIME | Timer for monitoring communication
I_b_StartRead | BOOL | TRUE (positive edge) = Start execution of read command
I_b_StartWrite | BOOL | TRUE (positive edge) = Start execution of write command
I_b_StartSpecialCommand | BOOL | TRUE (positive edge) = Start execution of special command (freely definable command)
I_b_UserMemory_UID | BOOL | FALSE = Access to user data area (user memory) TRUE = Access to Fixcode (UID)
I_b_EPC | BOOL | FALSE = no meaning; specified by I_b_UserMemory_UID TRUE = Access to EPC/UII area (UHF only)

## Slide 16: IC-KP2-2HB21 SingleFrame TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
I_b_SingleEnhanced | Bool | FALSE = Execution Single command (one-time execution) TRUE = Execution Enhanced command (permanent execution)
I_b_Quit | Bool | TRUE (positive edge) = Start execution of Quit command; abort of running Enhanced command
I_w_StartAddress | Word | Start address on data carrier
I_i_WordNumber | Integer | Number of addressed data blocks of 4 bytes each
I_w_TagType | Word | Data carrier type
O_b_Done | Bool | FALSE = Command is still active or not yet completed; data carrier outside detection zone TRUE = Command completed; data carrier within detection zone (Enhanced)
O_b_NoDataCarrier | Bool | FALSE = Data carrier within detection zone (Enhanced) TRUE = Data carrier outside detection zone (Single and Enhanced)

## Slide 17: IC-KP2-2HB21 SingleFrame TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
O_b_Busy | Bool | FALSE = no command active; negative edge = command ended TRUE = Command active or currently being executed
O_b_Finish | Bool | FALSE = Command is still active or not yet completed; TRUE = command completed
O_b_Error | Bool | FALSE = no error status TRUE = error status; error status on O_B_Status
O_B_Status | Byte | Status value of the command execution
O_B_ReplyCounter | Byte | Response counter
IO_b_SetRestart | Bool | TRUE (positive edge) = Start execution of initialization routine; set input back to False after one cycle
IO_b_InitFinish | Bool | TRUE = Initialization completed successfully; function module ready for operation
UserData | Data block | Data block for read and write data

## Slide 18: IC-KP2-2HB21 SingleFrame TwinCAT 3
Declaration of function and data block
IDENTControl_FB_Head1  Function block for channel 1 (Typ IDENTControl_SF)
IDENTControl_FB_Head2  Function block for channel 2 (Typ IDENTControl_SF)
Head1Data  Data block for channel 1
Head2Data  Data block for channel 2

## Slide 19: IC-KP2-2HB21 SingleFrame TwinCAT 3
Structure of data block IDENTControl_UserData
DUT IDENTControl_UserData
ReadData  contains the read data
WriteData  contains the write data
SpecialCommand  Data field for the freely definable command

## Slide 20: IC-KP2-2HB21 SingleFrame TwinCAT 3
Schematic representation of the blocks:
Function block
IDENTControl_FB_
Head1
Data block
Head1Data
Data block
Head2Data
UserData
Remark:
Function blocks IDENTControl_FB_Head1 and IDENTControl_FB_Head2 of type IDENTControl_SF
Data blocks Head1Data and Head2Data of type IDENTControl_UserData
Function block
IDENTControl_FB_
Head2
UserData

## Slide 21: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
Initialization must be carried out after device start-up
Assignment of the data carrier type to the I_w_TagType input (e.g. IQC21  16#3231 or factory setting  16#3939)
Start by positive edge on IO_b_SetRestart
Initialization successfully completed if signal change at IO_b_InitFinish to True
Before executing a new initialization, IO_b_SetRestart must be reset to False
All variables of the FB are reset; data blocks are overwritten with 16#00
All active Enhanced commands are canceled
Option for error acknowledgement

## Slide 22: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IPC02 | EM4102 (Unique) | 16#3032 | IPH-…-V1 (125kHz) | Single / Enhanced Read Fixcode
IPC03 | EM4450 (Titan) | 16#3033 | IPH-…-V1 (125kHz) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words
IPC11 | Q5 | 16#3131 | IPH-…-V1 (125kHz) | Single / Enhanced Read Fixcode Single / Enhanced Write Fixcode
IQC20 | Alle ISO15693 Datenträger | 16#3230 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode
IQC21 | NXP ICode SLI | 16#3231 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC22 | Texas Instruments Tag-It HF-I Plus | 16#3232 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)

## Slide 23: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IQC24 | Infineon my-D SRF55V10P | 16#3234 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC33 | Fujitsu MB89R118 | 16#3333 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC35 | NXP Icode SLI-S | 16#3335 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC37 | Fujitsu MB89R112 | 16#3337 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)

## Slide 24: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC72 | NXP U Code G2XM | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)
IUC76 | Alien Higgs-3 | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)

## Slide 25: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC77 | Impinj Monza 4QT | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)
IUC82 | NXP U Code 7xm-2k | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)

## Slide 26: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC87 | Alien Higgs-3 | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)
IUC88 | NXP U Code 9xm | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words (SpecialCommand) Single / Enhanced Write 16-Bit Words (SpecialCommand) Read / Write Parameter (SpecialCommand)

## Slide 27: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
Initialization routine:
Start via positive edge on IO_b_SetRestart
Reset input IO_b_SetRestart after at least one cycle
Initialization completed when IO_b_InitFinish = True (positive edge)
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the data carrier type was parameterized incorrectly
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 28: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#04 = Change Tag command
OUTDATA[3]  not used
OUTDATA[4]..[5]  TagType;, 16#3939 = Default setting
OUTDATA[6]….[x]  not used
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#04 = Change Tag command
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 29: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 1: Initialization

## Slide 30: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Single read attempt on the Fixcode (UID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := False
Start by positive edge on I_b_StartRead
Command ends after one read attempt
Read successful, Fixcode read; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (access to UID)
I_b_EPC := False (not relevant)
I_b_StartRead := True (start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read not successful, data carrier not recognized and Fixcode not read in:
I_b_SingleEnhanced := False
I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 31: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Data carrier recognized and Fixcode read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 32: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Data carrier recognized and Fixcode read
DB UserData.ReadData.ReadData[x]
ReadData[0] ...[7]  Fixcode (8 byte Fixcode; ISO15693)
ReadData[8]...[x]  16#00
The length of the Fixcode depends on the data carrier. All ISO15693 (13.56MHz) data carriers have a Fixcode with a length of 8 bytes. IPC02 has a Fixcode with a length of 5 bytes. IPC03 has a Fixcode with a length of 4 bytes. UHF data carriers have a TID with a length of 12 bytes

## Slide 33: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Input data field: Fixcode read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[15]  Fixcode (UID; ISO15693 data carrier)
INDATA[16]…[x]  not used

## Slide 34: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 35: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)
Output data field: Command Single Read Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]…[x]  not used

## Slide 36: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)

## Slide 37: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 2: Single Read Fixcode (UID)

## Slide 38: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Single read attempt on the user data area (User Memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start by positive edge on I_b_StartRead
Command ends after one read attempt
Read successful, data read in; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartRead := True (start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read not successful, data carrier not recognized and data not read in
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 39: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Data carrier recognized and user data read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 40: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Data carrier recognized and user data read:
DB UserData.ReadData.ReadData[x]
ReadData[0] ...[7]  Read data (2 blocks of 4 bytes each)
ReadData[8]...[x]  16#00
The number of blocks to be read in with a block size of 4 bytes each is defined via the input I_i_WordNumber
Note:
When using the IQC33, the I_i_WordNumber must always be a multiple of 2. This data carrier has a block size of 8 bytes.

## Slide 41: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Input data field: User data read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#10 = Single Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Number of transmitted data blocks of 4 bytes each (I_i_WordNumber)
INDATA[8]…[15]  User data read in
INDATA[16]…[x]  not used

## Slide 42: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#10 = Single Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 43: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words
Output data field: Command Single Read Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#10 = Single Read Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of data blocks (I_i_WordNumber)

## Slide 44: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words

## Slide 45: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 3: Single Read Words

## Slide 46: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Single write attempt to the user data area (User Memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Specify write data in WriteData
Start by positive edge on I_b_StartWrite
Write successful, data written; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write not successful, data carrier not recognized and data not written
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 47: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB UserData.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 48: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Data carrier recognized and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 49: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Input data field: User data written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#40 = Single Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 50: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#40 = Single Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 51: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words
Output data field: Command Single Write Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#40 = Single Write Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]…[15]  Write data
OUTDATA[16]…[x]  not used

## Slide 52: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words

## Slide 53: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 4: Single Write Words

## Slide 54: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Permanent read operation on the Fixcode (UID or TID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := True
Start by positive edge on I_b_StartRead
End of command execution via Quit command or initialization
Start read process; read process activated; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Read process activated; data carrier enters detection zone; Fixcode read:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process; read process activated; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel read process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 55: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Data carrier recognized and Fixcode read; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier detected; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 56: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Data carrier recognized and Fixcode read
DB UserData.ReadData.ReadData[x]
ReadData[0] ...[7]  Fixcode (8 byte Fixcode; ISO15693)
ReadData[8]...[x]  16#00
The length of the Fixcode depends on the data carrier. All ISO15693 (13.56MHz) data carriers have a Fixcode with a length of 8 bytes. IPC02 has a Fixcode with a length of 5 bytes. IPC03 has a Fixcode with a length of 4 bytes. UHF data carriers have a TID with a length of 12 bytes

## Slide 57: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Input data field: Fixcode read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[15]  Fixcode (UID; ISO15693 data carrier)
INDATA[16]…[x]  not used

## Slide 58: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Input data field: no data carrier detected or data carrier has left the detection zone
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier detected or data carrier has left detection zone
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 59: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Output data field: Command Enhanced Read Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]…[x]  not used

## Slide 60: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)

## Slide 61: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)

## Slide 62: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Permanent read operation on the user data area (user memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start I_b_StartRead; End via Quit command or initialization
Start read process; read process activated; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Read process activated; data carrier enters detection zone; data read:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process; read process activated; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Abort read process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 63: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Data carrier recognized and data read in; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier detected; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 64: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Data carrier recognized and user data read
DB UserData.ReadData.ReadData[x]
ReadData[0] ...[7]  Read data (2 blocks of 4 bytes each)
ReadData[8]...[x]  16#00
The number of blocks to be read in with a block size of 4 bytes each is defined via the input I_i_WordNumber
Note:
When using the IQC33, the I_i_WordNumber must always be a multiple of 2. This data carrier has a block size of 8 bytes.

## Slide 65: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Input data field: User data read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#19 = Enhanced Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Number of transmitted data blocks of 4 bytes each (I_i_WordNumber)
INDATA[8]…[15]  User data read in
INDATA[16]…[x]  not used

## Slide 66: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#19 = Enhanced Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 67: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words
Output data field: Command Enhanced Read Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#19 = Enhanced Read Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of data blocks (I_i_WordNumber)

## Slide 68: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words

## Slide 69: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 6: Enhanced Read Words

## Slide 70: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Permanent write operation to the user data area (user memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Write data WriteData; start via I_b_StartWrite; end via Quit command
Start write process; write process active; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Write process activated; data carrier enters detection zone; data written:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start write process; write process active; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel write process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 71: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB UserData.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 72: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Data carrier recognized and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 73: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Input data field: User data written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1A = Enhanced Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 74: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1A = Enhanced Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 75: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words
Output data field: Command Enhanced Write Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1A = Enhanced Write Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]…[15]  Write data
OUTDATA[16]…[x]  not used

## Slide 76: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words

## Slide 77: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 7: Enhanced Write Words

## Slide 78: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 8: Quit
Cancellation of active Enhanced commands
Start by positive edge on I_b_Quit
Start execution Quit:
I_b_Quit:= True  If the signal changes, a Quit command is executed and the active read command is canceled
Quit executed:
O_b_Done = True  Quit command completed
O_B_Status = 16#00

## Slide 79: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 8: Quit
Input data field: Quit command executed
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#02 = Quit command
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 80: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 8: Quit
Output data field: Quit command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#02 = Quit command
OUTDATA[3]…[x]  not used

## Slide 81: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 8: Quit

## Slide 82: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Only to be executed when using IUH-F19x-V1 (UHF system) with SingleFrame protocol
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := False
Start by positive edge on I_b_StartRead
Command ends after one read attempt
Read successful, UII/EPC read; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False
I_b_EPC := True (access to UII/EPC)
I_b_StartRead := True (Start read operation with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read not successful, data carrier not recognized and UII/EPC not read in:
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := True
I_b_StartRead := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 83: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Data carrier recognized and UII/EPC code read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 84: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Data carrier recognized and UII/EPC read in
DB UserData.ReadData.ReadData[x]
ReadData[0]...[1]  PC word
ReadData[2]...[13]  UII/EPC Code
The length of the UII/EPC code depends on the programming of the data carrier. In the majority of cases, the UII/EPC code has a length of 12 bytes. The length of the UII/EPC code is a multiple of 2 bytes. The PC word contains additional information about the programmed UII/EPC code.

## Slide 85: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Input data field: UII/EPC Code read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#D2 = Single Read UII
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[9]  PC Word
INDATA[10]…[21]  UII/EPC Code
INDATA[22]…[x]  not used

## Slide 86: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#D2 = Single Read UII
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 87: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)
Output data field: Command Single Read UII
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#D2 = Single Read UII
INDATA[3]…[x]  not used

## Slide 88: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)

## Slide 89: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 9: Single Read UII (EPC)

## Slide 90: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Only to be executed when using IUH-F19x-V1 (UHF system) with SingleFrame protocol
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := True
Start by positive edge on I_b_StartRead
End via Quit command or initialization
Start read process; read process activated; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := True
I_b_StartRead := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Read process activated; data carrier enters detection zone; UII/EPC read:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := True
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process; read process activated; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := True
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel read process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 91: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Data carrier recognized; UII/EPC read in; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier detected; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 92: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Data carrier recognized and UII/EPC read in
DB UserData.ReadData.ReadData[x]
ReadData[0]...[1]  PC word
ReadData[2]...[13]  UII/EPC Code
The length of the UII/EPC code depends on the programming of the data carrier. In the majority of cases, the UII/EPC code has a length of 12 bytes. The length of the UII/EPC code is a multiple of 2 bytes. The PC word contains additional information about the programmed UII/EPC code.

## Slide 93: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Input data field: UII/EPC Code read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#D3 = Enhanced Read UII
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[9]  PC Word
INDATA[10]…[21]  UII/EPC Code
INDATA[22]…[x]  not used

## Slide 94: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Input data field: no data carrier detected or data carrier has left the detection zone
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#D3 = Enhanced Read UII
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier detected or data carrier has left the detection zone
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 95: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)
Output data field: Command Enhanced Read UII
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#D3 = Enhanced Read UII
INDATA[3]…[x]  not used

## Slide 96: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)

## Slide 97: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 10: Enhanced Read UII (EPC)

## Slide 98: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Only to be executed when using IUH-F19x-V1 (UHF system) with SingleFrame protocol
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := False
I_w_Startaddress := 16#0000 and I_i_WordNumber := 14 (variable; depending on the length EPC)
Define write data in "WriteData”
Start by positive edge on I_b_StartWrite; command ends after one write attempt
Write successful, UII/EPC written; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (Access to UII/EPC)
I_b_StartWrite := True (Start write operation with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write not successful, data carrier not recognized and data not written
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := True
I_b_StartWrite := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 99: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Write data:
Assignment before the start of command execution
The write data consists of the PC word and the UII/EPC code
Assignment within the DB UserData.WriteData.WriteData[x]
Byte[0]...[1]  PC word
Byte[2]...[13]  UII/EPC Code
Byte[14]...[x]  not used
Number of write data depends on parameter I_i_NumberWords and includes the PC word and the UII/EPC code
The number is specified in terms of bytes
16#000E = 14 = 2 bytes PC word + 12 bytes UII/EPC

## Slide 100: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Data carrier recognized and UII/EPC successfully written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 101: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Input data field: UII/EPC Code written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#0D = Single Program Special Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 102: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#0D = Single Program Special Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 103: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)
Output data field: Command Single Program Special Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#0D = Single Program Special Fixcode
OUTDATA[3]  not used
OUTDATA[4]…[5]  not used
OUTDATA[6]…[7]  Number of bytes (I_i_WordNumber)
OUTDATA[8]…[9]  PC Word
OUTDATA[10]…[21]  UII/EPC Code
OUTDATA[22]…[x]  not used

## Slide 104: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)

## Slide 105: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 11: Single Program Special Fixcode (EPC)

## Slide 106: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Only to be executed when using IPH-...-V1 (LF system) with IPC11 data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_Startaddress := 16#0000 (not relevant) and I_i_WordNumber := 0 (not relevant)
Specify write data in "WriteData
Start by positive edge on I_b_StartWrite; command ends after one write attempt
Write successful, Fixcode written; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (Access to Fixcode)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (Start write operation with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write not successful, data carrier not recognized and Fixcode not written
I_b_SingleEnhanced := False
I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 107: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Write data:
Assignment before the start of command execution
The write data has a length of 5 bytes
Assignment within the DB UserData.WriteData.WriteData[x]
Byte[0]...[4]  Fixcode
Byte[5]...[x]  not used

## Slide 108: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Data carrier recognized and Fixcode successfully written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 109: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Input data field: Fixcode written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1F = Single Write Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 110: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1F = Single Write Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 111: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)
Output data field: Command Single Write Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1F = Single Write Fixcode
OUTDATA[3]  not used
OUTDATA[4]…[5]  Parameter <FixType>; 16#3131 = „11“ = Fixcode can be overwritten; preconfigured inside source code of function block
OUTDATA[6]…[7]  Number of bytes; preconfigured inside source code of function block
OUTDATA[8]…[12]  Fixcode
OUTDATA[13]…[x]  not used

## Slide 112: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)

## Slide 113: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 12: Single Write Fixcode (IPC11)

## Slide 114: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Permanent write operation to the Fixcode of an IPC11 data carrier (only for IPH-...-V1 LF system)
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (not relevant) and I_i_WordNumber := 0 (not relevant)
Write data “WriteData”; start via I_b_StartWrite; end via Quit command
Start write process; write process active; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Write process activated; data carrier enters detection zone; fixed code written:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start write process; write process active; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel write process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 115: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Write data:
Assignment before the start of command execution
The write data has a length of 5 bytes
Assignment within the DB UserData.WriteData.WriteData[x]
Byte[0]...[4]  Fixcode
Byte[5]...[x]  not used

## Slide 116: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Data carrier recognized and Fixcode written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 117: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Input data field: Fixcode written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#24 = Enhanced Write Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 118: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#24 = Enhanced Write Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 119: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)
Output data field: Command Enhanced Write Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#24 = Enhanced Write Fixcode
OUTDATA[3]  not used
OUTDATA[4]…[5]  Parameter <FixType>; 16#3131 = „11“ = Fixcode can be overwritten; preconfigured inside source code of function block
OUTDATA[6]…[7]  Number of bytes; preconfigured inside source code of function block
OUTDATA[8]…[12]  Fixcode
OUTDATA[13]…[x]  not used

## Slide 120: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)

## Slide 121: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 13: Enhanced Write Fixcode (IPC11)

## Slide 122: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed:
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 123: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB UserData.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BE = Command Read Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#51 = Q = System Q
Byte[4]...[5]  Parameter code; 16#5054 = PT = Transmit power
Byte[6]...[7]  Parameter length

## Slide 124: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 125: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
Transmission power read
DB UserData.ReadData.ReadData[x]
ReadData[0] ...[1]  16#0004 = Maximum

## Slide 126: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
Input data field: transmission power read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BE = Read Parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Length parameter; 16#0002 = 2 Byte
INDATA[8]…[9]  transmission power; 16#0004 = Maximum
INDATA[10]…[x]  not used

## Slide 127: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power
Output data field: Command Read Parameter
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BE = Read Parameter
OUTDATA[3]…[4]  not used
OUTDATA[5]  System Code; 16#51 = „Q“ = System Q
OUTDATA[6]…[7]  Parameter sign; 16#5054 = PT = transmission power
OUTDATA[8]…[9]  Length Parameter

## Slide 128: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 14: Special Command  Read out transmission power

## Slide 129: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed:
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 130: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB UserData.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BF = Command Write Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#51 = Q = System Q
Byte[4]...[5]  Parameter code; 16#5054 = PT = Transmit power
Byte[6]...[7]  Parameter length
Byte[8]...[9]  Parameter data; 16#0003 = Power level 3

## Slide 131: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 132: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power
Input data field: setup transmission power finished
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BF = Write Parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 133: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power
Output data field: Command Write Parameter
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BF = Write Parameter
OUTDATA[3]…[4]  not used
OUTDATA[5]  System Code; 16#51 = „Q“ = System Q
OUTDATA[6]…[7]  Parameter sign; 16#5054 = PT = transmission power
OUTDATA[8]…[9]  Length Parameter
OUTDATA[10]…[11]  Parameter data; 16#0003 = transmission power
level 3
OUTDATA[12]…[x]  not used

## Slide 134: IC-KP2-2HB21 SingleFrame TwinCAT 3
Example 15: Special Command  Setup transmission power

## Slide 135: Contact
Karsten Reinhardt
kreinhardt@de.pepperl-fuchs.com
+49 (0) 621 776 1736

## Slide 136: IC-KP2-2HB21 SingleFrame TwinCAT 3
Version history:
V1.0 26.09.2024
Initial Version