## Slide 2: Commissioning function block IC-KP2-2HB21-2V1D + IUH-F19x-V1-FRx-xx
TwinCAT 3 function block for the evaluation unit
IC-KP2-2HB21-2V1D (EtherCAT) with MultiFrame protocol for connecting the RFID devices IUH-F19x-V1-FRx-xx

## Slide 3: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
This documentation is valid with the following specification:
Beckhoff PLC and TwinCAT 3 programming environment
MultiFrame Protocol
Valid for the system IU (868MHz....920MHz; UHF) for connecting the devices IUH-F190-V1-FRx-xx and IUH-F192-V1-FRx with configuration protocol mode QV "MultiFrame"
Specified values for the UHF parameters apply to the IUH-F190-V1-FR1-01 device  Other parameter values apply depending on the RFID devices used
IDENTControl IC-KP2-2HB21-2V1D (EtherCAT)

## Slide 4: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Content Download:
PLC project with function block
Export source code
Version history
Documentation (DEU, ENG)

## Slide 5: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Table of contents:
Scanning for connected devices
Link to process data
Change EtherCAT telegram length
Read out firmware version
Configuration of process data fields
Inputs and outputs function block
Declaration of function and data block
Structure of data block
Schematic diagram of building blocks
Example 1: Initialization Setup Tag Type
Example 2: Single Read UII/EPC one-time read access to the UII/EPC Code (Memory Bank 01)
Example 3: Single Read Fixcode (TID) one-time read access to the Fixcode (TID) (Memory Bank 10)
Example 4: Single Read Words one-time read access to the User Memory (Memory Bank 11)
Example 5: Single Write UII/EPC one-time write access to the UII/EPC Code (Memory Bank 01)
Example 6: Single Write Words one-time write access to the User Memory (Memory Bank 11)
Example 7: Enhanced Read UII/EPC continuous read access to the UII/EPC Code (Memory Bank 01)
Example 8: Enhanced Read Fixcode (TID) continuous read access to the Fixcode (TID) (Memory Bank 10)
Example 9: Enhanced Read Words continuous read access to the User Memory (Memory Bank 11)
Example 10: Enhanced Write Words continuous write access to the User Memory (Memory Bank 11)
Example 11: Quit stop of an Enhanced command
Example 12: Special Command  Read out transmission power Execution of freely definable command
Example 13: Special Command  Reset to factory setting IUH-F19x-V1 Execution of freely definable command
Example 14: Read out UHF Parameter IUH-F19x-V1 Read access to all UHF parameter
Example 15: Change UHF Parameter IUH-F19x-V1 Write access to all UHF parameter (predefined with factory setting of IUH-F190-V1-FR1-01)
Parameter IF - additional information Parameter AP – antenna polarization Parameter CD – sending channels Parameter E5 – enhanced status 5
Parameter MB – memory bank Parameter NT – number of tags Parameter QV – protocol mode Parameter QW – Q value
Parameter SM – sensing mode Parameter TA – tries allowed Parameter PT – power transmit Parameter MF – measured reflection Parameter RC – region code Parameter NC – number channels Parameter FL – filter list Parameter SE – session
Parameter FB – search mode Parameter FR – first read Parameter EF – fixcode length

## Slide 6: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Scanning for connected devices
Activate Config Mode
Right-click on "Device 5 (EtherCAT)"  Scan  IDENTControl with the telegram length set in the device appears

## Slide 7: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Link process data field input data
Activate Config Mode
Right-click on "IN_CH1"  Change link  Activate array mode
 GVL_IDENTControl.BUS_INPUT[1]  Link from byte 0
to byte 63

## Slide 8: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Link process data field output data
Activate Config Mode
Right-click on "OUT_CH1“  Change link  Activate array mode  GVL_IDENTControl.BUS_OUTPUT[1]  Link from byte 0
to byte 63

## Slide 9: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Change EtherCAT telegram length
Activate Config Mode  Scan to detect connected device  Double-click on the "IDENTControl Compact 64 Byte IN/OUT" module  EtherCAT  Advanced settings

## Slide 10: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Change EtherCAT telegram length
ESC access  EEPROM  Smart View  Write EEPROM  Select new module size

## Slide 11: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Change EtherCAT telegram length
Remove module  Scan  Module read in with new telegram length  Link process data

## Slide 12: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Read out firmware version
Double-click on IDENTControl Compact module  CoE - Online

## Slide 13: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Configuration of process data fields
Definition as global variables (GVL)
BUS_OUTPUT = Output data field
BUS_INPUT = input data field
Multidimensional array with a length of 254 bytes

## Slide 14: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Inputs and outputs function block:

## Slide 15: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
pADR_IN | PVOID | Address Input data field channel 1 or 2
cbSIZE_IN | UDINT | Length of input data field channel 1 or 2
pADR_OUT | PVOID | Address Output data field channel 1 or 2
cbSIZE_OUT | UDINT | Length of output data field channel 1 or 2
I_T_Timeout | TIME | Timer for monitoring communication
I_b_StartRead | BOOL | TRUE (positive edge) = Start execution of read command
I_b_StartWrite | BOOL | TRUE (positive edge) = Start execution of write command
I_b_StartSpecialCommand | BOOL | TRUE (positive edge) = Start execution of special command (freely definable command)
I_b_UserMemory_UID | BOOL | FALSE = Access to user data area (user memory) TRUE = Access to fixcode (UID or TID)
I_b_EPC | BOOL | FALSE = no meaning; specified by I_b_UserMemory_UID TRUE = Access to EPC/UII area (UHF only)

## Slide 16: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
I_b_SingleEnhanced | Bool | FALSE = Execution Single command (one-time execution) TRUE = Execution Enhanced command (permanent execution)
I_b_Quit | Bool | TRUE (positive edge) = Start execution of Quit command; abort of running Enhanced command
I_w_StartAddress | Word | Start address on data carrier
I_i_WordNumber | Integer | Number of addressed data blocks of 2 bytes each
I_w_TagType | Word | Data carrier type; 16#3830 (Tag Type 80)
I_b_WriteParameter | Bool | FALSE = Execution read access to parameter TRUE = Execution write access to parameter
O_b_Done | Bool | FALSE = Command is still active or not yet completed; data carrier outside detection zone TRUE = Command completed; data carrier within detection zone (Enhanced)
O_b_NoDataCarrier | Bool | FALSE = Data carrier within detection zone (Enhanced) TRUE = Data carrier outside detection zone (Single and Enhanced)
O_b_Busy | Bool | FALSE = no command active; negative edge = command ended TRUE = Command active or currently being executed

## Slide 17: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Inputs and outputs function block:
Name | Type | Meaning
O_b_Finish | Bool | FALSE = Command is still active or not yet completed; TRUE = command completed;
O_b_Error | Bool | FALSE = no error status TRUE = error status; error status on O_B_Status
O_B_Status | Byte | Status value of the command execution 16#00 = data read/written; 16#04 = parameter error; 16#05 = tag has left detection zone; 16#06 = no connection to RFID device; 16#0A = several tags with the same UII/EPC
O_B_ReplyCounter | Byte | Response counter
O_b_EndConfig | Bool | TRUE = Parameter access completed
IO_b_SetRestart | Bool | TRUE (positive edge) = Start execution of initialization routine; set input back to False after one cycle
IO_b_InitFinish | Bool | TRUE = Initialization completed successfully; function module ready for operation
IO_b_StartConfig | Bool | TRUE = Start parameter access
IO_b_NewData | Bool | TRUE = new telegram received (direct reset by user required)
UserDataGlobal | Data block | Data block for read and write data

## Slide 18: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Status values:
O_B_Status | Meaning | Remark
16#00 | Data successfully read/written (read/write command); command successfully executed (read/write parameter command) | Telegram contains information read in from the data carrier; in the case of read access, this is the UII/EPC code and a sub-area of the user memory or the TID; if only the UII/EPC is accessed, the other information is omitted When identifying several data carriers at the same time, the information read in is transmitted in separate telegrams one after the other
16#04 | Parameter error; command parameter out of specification; data carrier memory size does not match the command configuration | If the memory size is too small when accessing a data carrier, a status 16#04 message and the UII/EPC of the corresponding data carrier are returned When accessing a parameter, it must be taken into account that different parameters are supported depending on the device version and that the value ranges can be different  O_b_Error = True
16#05 | Data carrier has left the detection zone | Only sent when an Enhanced (permanent) command is executed; telegram contains the UII/EPC of the data carrier that has left the detection zone; this message can be delayed using parameter E5
16#06 | RFID device not connected or communication between RFID device and evaluation unit interrupted | If a command is sent on a channel to which no RFID device is connected, a status 16#06 telegram is reported back; if communication to the RFID device is interrupted during the execution of an enhanced (permanent) command, a status 16#06 telegram is reported back  O_b_Error = True
16#0A | Multiple data carriers with the same UII/EPC code in the detection zone | When identifying several data carriers simultaneously in the detection zone, all data carriers must have a unique (different) UII/EPC code; if several (>1) data carriers have an identical UII/EPC, a status 16#0A message is returned  O_b_Error = True
16#0B | Telegram with additional information about data carrier access | The IF (additional information) parameter can be used to activate the transmission of additional information about data carrier access; this information is transmitted directly after a status 16#00 telegram via a status 16#0B telegram; transmission is switched off by default
16#0F | End of single command; telegram contains the number of data carriers identified during command execution | The end of the command execution of a single command is signaled via a status 16#0F telegram; this telegram contains the number of identified data carriers; no data carrier = 16#3030_3030; 1 data carrier = 16#3030_3031; 2 data carriers = 16#30303032 etc.

## Slide 19: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Declaration of function and data block
IC_KP2_2HB21_IUH_MF_Head1  Function block for channel 1 (Type IC_KP2_2HB21_IUH_MF)
IC_KP2_2HB21_IUH_MF_Head2  Function block for channel 2 (Type IC_KP2_2HB21_IUH_MF)
Head1Data  Data block for channel 1 (Type IDENTControl_UserData_IUH_MF)
Head2Data  Data block for channel 2 (Type IDENTControl_UserData_IUH_MF)

## Slide 20: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Structure of data block IDENTControl_UserData_IUH_MF
DUT IDENTControl_UserData
ReadData  contains the read data
WriteData  Contains the write data
SpecialCommand  Data field for the freely definable command
NumberTags  contains the number of data carriers identified within a single command
TagInformation  contains additional information about the data carrier access
EPC_WrittenTag  contains the UII/EPC code of the successfully written data carrier
EPC_Leave_Tag  contains the UII/EPC code of a data carrier that left the detection zone when an Enhanced command was executed
ReadParam_XX  Current parameter value; WriteParam_XX  New parameter value

## Slide 21: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Structure data block IDENTControl_UserData_IUH_MF

## Slide 22: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Schematic diagram of building blocks:
Data block
Head1Data
Data block
Head2Data
Note:
Function blocks IC_KP2_2HB21_IUH_MF_Head1 and IC_KP2_2HB21_IUH_MF_Head2 from type IC_KP2_2HB21_IUH_MF
Data blocks
Head1Data and Head2Data from type IDENTControl_UserData_IUH_MF
Function block
IC_KP2_2HB21_IUH_MF_Head1
Function block
IDENTControl_FB_MF
UserDataGlobal
Function block
IC_KP2_2HB21_IUH_MF_Head2
Function block
IDENTControl_FB_MF
UserDataGlobal

## Slide 23: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
Initialization must be carried out after device start-up
Assignment of the data carrier type to the I_w_TagType input (e.g. IUCxx  16#3830 or factory setting  16#3939)
Valid for all UHF data carriers
Start by positive edge on IO_b_SetRestart
Initialization successfully completed if signal change at IO_b_InitFinish to True
Before executing a new initialization, IO_b_SetRestart must be reset to False
All variables of the FB are reset; data blocks are overwritten with 16#00
All active Enhanced commands are canceled (with Tag Type = 16#3830)
Option for error acknowledgement

## Slide 24: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC72 | NXP U Code G2XM | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)
IUC76 | Alien Higgs-3 | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)

## Slide 25: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC77 | Impinj Monza 4QT | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)
IUC82 | NXP U Code 7xm-2k | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)

## Slide 26: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID Device | Commands
IUC87 | Alien Higgs-3 | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)
IUC88 | NXP U Code 9xm | 16#3830 | IUH-F19x-V1-FRx (ISO18000-63) | Single / Enhanced Read Fixcode Single / Enhanced Read Words (SpecialCommand) Single / Enhanced Write Words (SpecialCommand) Single / Enhanced Read Special Fixcode Single Program Special Fixcode Single / Enhanced Read 16-Bit Words Single / Enhanced Write 16-Bit Words Read / Write Parameter (SpecialCommand)

## Slide 27: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
Initialization routine:
Start via positive edge on IO_b_SetRestart
Reset input IO_b_SetRestart after at least one cycle
Initialization completed when IO_b_InitFinish = True (positive edge)
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the data carrier type was parameterized incorrectly
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 28: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#04 = Change Tag command
OUTDATA[3]  not used
OUTDATA[4]..[5]  Tag Type;, 16#3830 = IUCxx data carrier; all UHF data carrier
OUTDATA[6]….[x]  not used
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#04 = Change Tag command
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 29: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 1: Initialization

## Slide 30: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Single read attempt on the UII/EPC code of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := False
Start by positive edge on I_b_StartRead
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Command ends after one read attempt
Read successful, UII/EPC read; no transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := True
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)

## Slide 31: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Read successful, UII/EPC read; transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := True
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Receive additional information from Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)

## Slide 32: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Read not successful, UII/EPC not read; command terminated:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := True
StartRead := True
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = True
Status = 16#0F
NewData = True (0  1)

## Slide 33: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Data carrier identified and UII/EPC code read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F
No data carrier identified:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F

## Slide 34: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Data carrier identified and UII/EPC code read in
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC Word + 12 bytes UII/EPC Code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length could be variable and dependents on the initial programming of the data carrier

## Slide 35: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Data carrier identified and UII/EPC read in; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission power level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00 telegram).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was identified

## Slide 36: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Data carrier identified and UII/EPC code read; number of data carriers identified during the execution of the single command
DB Head1Data.NumberTags.NumberTags[x]
NumberTags[0]...[3]  Number of data carriers in ASCII
NumberTags[0]...[3] = 16#30303031 = "0001" = 1 data carrier
NumberTags[0]...[3] = 16#30303032 = "0002" = 2 data carriers
NumberTags[0]...[3] = 16#30303033 = "0003" = 3 data carriers
NumberTags[0]...[3] = 16#30303030 = "0000" = no data carrier

## Slide 37: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC
Output data field: Single Read UII command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#D2 = Single Read UII
OUTDATA[3]...[x]  not used

## Slide 38: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC

## Slide 39: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 2: Single Read UII/EPC

## Slide 40: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Single read attempt on the fixcode (TID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := False
Start by positive edge on I_b_StartRead
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Command ends after one read attempt
Read successful, fixcode (TID) read; no transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (access to TID resp. Fixcode)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := True
EPC := False
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)

## Slide 41: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Read successful, fixcode (TID) read; transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (access to TID resp. Fixcode)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := True
EPC := False
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)

## Slide 42: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Read not successful, fixcode (TID) not read; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (access to TID resp. Fixcode)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := True
EPC := False
StartRead := True
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = True
Status = 16#0F
NewData = True (0  1)

## Slide 43: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Data carrier identified and fixcode read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F
No data carrier identified:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F

## Slide 44: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Data carrier identified and fixcode (TID) read in
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
ReadData[16] ...[17]  Length of fixed code (TID); 16#000C = 12 bytes
ReadData[18] ...[29]  Fixcode (TID); length depends on the chip type
When using the MultiFrame protocol, the UII/EPC code of the identified data carrier is placed in front of the information read in. This makes it possible to clearly assign the read data record to a data carrier.
The length of the TID depends on the chip used. In the majority of cases, the TID has a length of 12 bytes. The first byte of the TID always has the value 16#E2. The chip type of the data carrier used can be determined by reading out the TID.

## Slide 45: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Data carrier identified and fixcode (TID) read; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission power level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00 telegram).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was identified

## Slide 46: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Data carrier identified and fixcode (TID) read; number of data carriers identified during the execution of the single command
DB Head1Data.NumberTags.NumberTags[x]
NumberTags[0]...[3]  Number of data carriers in ASCII
NumberTags[0]...[3] = 16#30303031 = "0001" = 1 data carrier
NumberTags[0]...[3] = 16#30303032 = "0002" = 2 data carriers
NumberTags[0]...[3] = 16#30303033 = "0003" = 3 data carriers
NumberTags[0]...[3] = 16#30303030 = "0000" = no data carrier

## Slide 47: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)
Output data field: command Single Read Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#01 = Single Read Fixcode
OUTDATA[3]…[x]  not used

## Slide 48: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)

## Slide 49: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 3: Single Read Fixcode (TID)

## Slide 50: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Single read attempt on the user data area (user memory) of a data carrier; access to 2-byte data blocks
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 4 (variable)
Start by positive edge on I_b_StartRead
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Command ends after one read attempt
Read successful, user memory read; no transfer of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := False
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)

## Slide 51: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Read successful, user memory read; transfer of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := False
StartRead := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)

## Slide 52: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Read not successful, user memory not read; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartRead := True (Start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False
Start read process:
SingleEnhanced := False
User_UID := False
EPC := False
StartRead := True
End read process:
Busy = False
Done = True
Finish = True
NoDataCarrier = True
Status = 16#0F
NewData = True (0  1)

## Slide 53: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Data carrier identified and user data read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F
No data carrier identified:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F

## Slide 54: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Data carrier identified and user memory read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
ReadData[16] ...[17]  Length of read sub-area user memory; 16#0008 = 8 bytes
ReadData[18] ...[25]  User memory; length depends on I_i_WordNumber
When using the MultiFrame protocol, the UII/EPC code of the identified data carrier is placed in front of the information read in. This makes it possible to clearly assign the read data record to a data carrier.

## Slide 55: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Data carrier identified and user memory read; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 56: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Data carrier identified and user memory read; number of data carriers identified during the execution of the single command
DB Head1Data.NumberTags.NumberTags[x]
NumberTags[0]...[3]  Number of data carriers in ASCII
NumberTags[0]...[3] = 16#30303031 = "0001" = 1 data carrier
NumberTags[0]...[3] = 16#30303032 = "0002" = 2 data carriers
NumberTags[0]...[3] = 16#30303033 = "0003" = 3 data carriers
NumberTags[0]...[3] = 16#30303030 = "0000" = no data carrier

## Slide 57: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words
Output data field: Single Read Words command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#49 = Single Read 2-Byte Words
OUTDATA[3]  not used
OUTDATA[4]...[5]  Start address (I_w_StartAddress)
OUTDATA[6]...[7]  Number of 2-byte data words (I_i_WordNumber)

## Slide 58: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words

## Slide 59: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 4: Single Read Words

## Slide 60: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Single write attempt to the UII/EPC code of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (not relevant) and I_i_WordNumber := 14 (variable)
Set write data in WriteData; start by positive edge on I_b_StartWrite
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Write successful, UII/EPC programmed; no transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Start write process:
SingleEnhanced := False
User_UID := False
EPC := True
StartWrite := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)

## Slide 61: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Write successful, UII/EPC code programmed; transmission of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start write process:
SingleEnhanced := False
User_UID := False
EPC := True
StartWrite := True
Receive of read-in data (UII/EPC code of the programmed data carrier) Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)

## Slide 62: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Write not successful, UII/EPC code not programmed; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := True (access to UII/EPC Code)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False
Start write process:
SingleEnhanced := False
User_UID := False
EPC := True
StartWrite := True
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = True
Status = 16#0F
NewData = True (0  1)

## Slide 63: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Write data:
Assignment before the start of command execution
Assignment within the DB Head1Data.WriteData.WriteData[x]
Byte[0]...[1]  PC word
Byte[2]...[x]  UII/EPC Code
The parameter "I_i_NumberWords" describes the number of bytes for the write data
The write data consists of the PC word and the UII/EPC code
The PC word has a different value depending on the length of the UII/EPC code

## Slide 64: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Data carrier identified and UII/EPC written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F
No data carrier identified:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F

## Slide 65: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Data carrier identified and UII/EPC successfully written
DB Head1Data.EPC_WrittenTag.EPC_WrittenTaga[x]
EPC_WrittenTag[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
EPC_WrittenTag[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
EPC_WrittenTag[4] ...[15]  UII/EPC code of the written data carrier; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the programmed transponder is sent back when a write access to a data carrier is successfully executed. This makes it possible to clearly assign the write process to a data carrier.

## Slide 66: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Data carrier identified and UII/EPC written; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 67: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Data carrier identified and UII/EPC written; number of data carriers identified during the execution of the single command
DB Head1Data.NumberTags.NumberTags[x]
NumberTags[0]...[3]  Number of data carriers in ASCII
NumberTags[0]...[3] = 16#30303031 = "0001" = 1 data carrier
NumberTags[0]...[3] = 16#30303030 = "0000" = no data carrier
When executing a write access to the UII/EPC code of a data carrier, only one data carrier may be in the detection zone at any one time

## Slide 68: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC
Output data field: Single Program Special Fixcode command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#0D = Single Program Special Fixcode
OUTDATA[3]  not used
OUTDATA[4]...[5]  not used
OUTDATA[6]...[7]  Number of bytes (I_i_WordNumber)
OUTDATA[8]...[9]  PC word
OUTDATA[10]...[21]  UII/EPC Code
OUTDATA[22]...[x]  not used

## Slide 69: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC

## Slide 70: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 5: Single Write UII/EPC

## Slide 71: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Single write attempt to the user data area (User Memory) of a data carrier; access to 2-byte data blocks
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 4 (variable)
Set write data in WriteData; start by positive edge on I_b_StartWrite
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Write successful, user memory programmed; no transfer of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Start write process:
SingleEnhanced := False
User_UID := False
EPC := False
StartWrite := True
Receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)

## Slide 72: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Write successful, user memory programmed; transfer of additional information; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start write process:
SingleEnhanced := False
User_UID := False
EPC := False
StartWrite := True
Receive of read-in data (UII/EPC code of the programmed data carrier) Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#0F
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)

## Slide 73: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Write not successful, user memory not programmed; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (Start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False
Start write process:
SingleEnhanced := False
User_UID := False
EPC := False
StartWrite := True
End write process:
Busy = False
Done = True
Finish = True
NoDataCarrier = True
Status = 16#0F
NewData = True (0  1)

## Slide 74: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB Head1Data.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 75: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Data carrier identified and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F
No data carrier identified:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#0F

## Slide 76: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Data carrier identified and user memory successfully written
DB Head1Data.EPC_WrittenTag.EPC_WrittenTaga[x]
EPC_WrittenTag[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
EPC_WrittenTag[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
EPC_WrittenTag[4] ...[15]  UII/EPC code of the written data carrier; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the programmed transponder is sent back when a write access to a data carrier is successfully executed. This makes it possible to clearly assign the write process to a data carrier.

## Slide 77: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Data carrier identified and user memory written; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 78: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Data carrier detected and user memory written; number of data carriers identified during the execution of the single command
DB Head1Data.NumberTags.NumberTags[x]
NumberTags[0]...[3]  Number of data carriers in ASCII
NumberTags[0]...[3] = 16#30303031 = "0001" = 1 data carrier
NumberTags[0]...[3] = 16#30303032 = "0002" = 2 data carriers
NumberTags[0]...[3] = 16#30303033 = "0003" = 3 data carriers
NumberTags[0]...[3] = 16#30303030 = "0000" = no data carrier

## Slide 79: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words
Output data field: Single Write Words command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#4A = Single Write 2-Byte Words
OUTDATA[3]  not used
OUTDATA[4]...[5]  Start address (I_w_StartAddress)
OUTDATA[6]...[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]...[15]  Write data
OUTDATA[16]...[x]  not used

## Slide 80: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words

## Slide 81: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 6: Single Write Words

## Slide 82: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Continuous read operation on the UII/EPC code of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := True and I_b_SingleEnhanced := True
Start by positive edge on I_b_StartRead
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
End of command execution via Quit command or initialization
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := True
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := True
StartRead := True
Status = 16#00
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 83: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := True
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; Tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := True
StartRead := True
Status = 16#00
NewData = True (0  1)
Receive additional information Tag B:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 84: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Data carrier identified UII/EPC code read; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00 or 16#0B
No data carrier identified/ tag leave zone; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 85: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Data carrier identified and UII/EPC code read in
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC Word + 12 bytes UII/EPC Code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC Code; length variable and dependent on the initial programming of the data carrier

## Slide 86: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Data carrier identified and UII/EPC code read; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 87: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Data carrier has left the detection zone
DB Head1Data.EPC_LeaveTag.EPC_LeaveTag[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the data carrier is transmitted via a status 16#05 telegram when an Enhanced command is executed as soon as this data carrier has left the detection zone

## Slide 88: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC
Output data field: Enhanced Read UII/EPC Code command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#D3 = Enhanced Read UII
OUTDATA[3]...[x]  not used

## Slide 89: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC

## Slide 90: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 7: Enhanced Read UII/EPC

## Slide 91: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Continuous read operation on the fixcode (TID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := True
Start by positive edge on I_b_StartRead
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
End of command execution via Quit command or initialization
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := True
EPC := False
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; tag inside detection zone:
SingleEnhanced := True
User_UID := True
EPC := False
StartRead := True
Status = 16#00
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 92: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := True
EPC := False
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; tag inside detection zone:
SingleEnhanced := True
User_UID := True
EPC := False
StartRead := True
Status = 16#00
NewData = True (0  1)
Receive additional information Tag B:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 93: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Data carrier identified and fixcode read in; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00 or 16#0B
No data carrier identified/ tag leave zone; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 94: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Data carrier identified and Fixcode (TID) read in
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
ReadData[16] ...[17]  Length of fixed code (TID); 16#000C = 12 bytes
ReadData[18] ...[29]  Fixcode (TID); length depends on the chip type
When using the MultiFrame protocol, the read information is preceded by the UII/EPC code of the identified data carrier. This makes it possible to clearly assign the read data record to a data carrier.
The length of the TID depends on the chip used. In the majority of cases, the TID has a length of 12 bytes. The first byte of the TID always has the value 16#E2. The chip type of the data carrier used can be determined by reading out the TID.

## Slide 95: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Data carrier identified and Fixcode (TID) read; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 96: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Data carrier has left the detection zone
DB Head1Data.EPC_LeaveTag.EPC_LeaveTag[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the data carrier is transmitted via a status 16#05 telegram when an Enhanced command is executed as soon as this data carrier has left the detection zone

## Slide 97: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)
Output data field: Single Read Fixcode command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
OUTDATA[3]...[x]  not used

## Slide 98: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)

## Slide 99: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 8: Enhanced Read Fixcode (TID)

## Slide 100: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Continuous read operation on the user data area (user memory) of a data carrier; access to 2-byte data blocks
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start by positive edge on I_b_StartRead; end via Quit command or initialization
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartRead := True
Status = 16#00
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 101: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Start read process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartRead := True
Status = 16#05
NewData = True (0  1)
Tag in the detection zone; receive of read in data Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Cancel read process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start read process; read process active; tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartRead := True
Status = 16#00
NewData = True (0  1)
Receive additional information Tag B:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Read process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 102: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Data carrier identified and data read in; command active :
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00 or 16#0B
No data carrier identified/ tag leave zone; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 103: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Data carrier identified and user memory read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  Length of UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
ReadData[16] ...[17]  Length of read sub-area user memory; 16#0008 = 8 bytes
ReadData[18] ...[25]  User memory; length depends on I_i_WordNumber
When using the MultiFrame protocol, the UII/EPC code of the identified data carrier is placed in front of the information read in. This makes it possible to clearly assign the read data record to a data carrier.

## Slide 104: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Data carrier identified and user memory read; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 105: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Data carrier has left the detection zone
DB Head1Data.EPC_LeaveTag.EPC_LeaveTag[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the data carrier is transmitted via a status 16#05 telegram when an Enhanced command is executed as soon as this data carrier has left the detection zone

## Slide 106: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words
Output data field: Enhanced Read Words command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#4B = Enhanced Read 2-Byte Words
OUTDATA[3]  not used
OUTDATA[4]...[5]  Start address (I_w_StartAddress)
OUTDATA[6]...[7]  Number of 2-byte data words (I_i_WordNumber)

## Slide 107: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words

## Slide 108: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 9: Enhanced Read Words

## Slide 109: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Continuous write operation to the user data area (user memory) of a data carrier; access to 2-byte data blocks
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start by positive edge on I_b_StartWrite; end via Quit command or initialization
Receipt of new data is signaled via signal change 0  1 at IO_b_NewData
Reset of IO_b_NewData by the user
Start write process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartWrite := True
Status = 16#05
NewData = True (0  1)
Tag inside detection zone; receive UII/EPC Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Cancel write process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start write process; write process active; Tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartWrite := True
Status = 16#00
NewData = True (0  1)
Write process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 110: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Start write process; no tag in the detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartWrite := True
Status = 16#05
NewData = True (0  1)
Tag inside detection zone; receive UII/EPC Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Receive additional information Tag A:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Cancel write process via Quit
Quit := True
Busy = False
Done = True
Finish = True
NoDataCarrier = False
Status = 16#00
NewData = True (0  1)
Start write process; write process active; Tag inside detection zone:
SingleEnhanced := True
User_UID := False
EPC := False
StartWrite := True
Status = 16#00
NewData = True (0  1)
Receive additional information Tag B:
Busy = True
Done = True
Finish = False
NoDataCarrier = False
Status = 16#0B
NewData = True (0  1)
Write process active; Tag leave detection zone
Busy = True
Done = False
Finish = False
NoDataCarrier = True
Status = 16#05
NewData = True (0  1)

## Slide 111: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB Head1Data.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 112: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Data carrier identified and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00 or 16#0B
No data carrier identified:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 113: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Data carrier identified and user memory successfully written
DB Head1Data.EPC_WrittenTag.EPC_WrittenTaga[x]
EPC_WrittenTag[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC Word + 12 bytes UII/EPC Code)
EPC_WrittenTag[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
EPC_WrittenTag[4] ...[15]  UII/EPC code of the written data carrier; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the programmed transponder is sent back after a successful write access to a data carrier. This makes it possible to clearly assign the write process to a data carrier.

## Slide 114: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Data carrier identified and user memory written; additional information about data carrier access
DB Head1Data.TagInformation.TagInformation[x]
TagInformation[0]  Information type; always 16#01
TagInformation[1]  RSSI value; signal strength between 16#00 (weak) and 16#64 (good); value range between 0 and 100
TagInformation[2]  Channel number of the transmission channels on which the data carrier was accessed (parameters CD and NC)
TagInformation[3]...[4]  Transmission line level at which the data carrier was accessed
When using the MultiFrame protocol, the transmission of additional information about the data carrier access must be activated via the IF parameter (IF := 16#01). The additional information is transmitted in a separate telegram with the status value 16#0B directly after the information received from the data carrier (status 16#00).
The additional information can be used to estimate the quality of data carrier access. Small values of the RSSI mean a lower quality or a greater distance.
When using several power levels (parameter PT), the additional information can be used to find out at which power level the data carrier was recognized.

## Slide 115: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Data carrier has left the detection zone
DB Head1Data.EPC_LeaveTag.EPC_LeaveTag[x]
ReadData[0] ...[1]  Length UII/EPC information; 16#000E = 14 bytes (2 bytes PC word + 12 bytes UII/EPC code)
ReadData[2] ...[3]  PC Word (contains additional information about the UII/EPC code)
ReadData[4] ...[15]  UII/EPC code; length variable and dependent on the initial programming of the data carrier
When using the MultiFrame protocol, the UII/EPC code of the data carrier is transmitted via a status 16#05 telegram when an Enhanced command is executed as soon as this data carrier has left the detection zone

## Slide 116: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words
Output data field: Enhanced Write Words command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#4C = Enhanced Write 2-Byte Words
OUTDATA[3]  not used
OUTDATA[4]...[5]  Start address (I_w_StartAddress)
OUTDATA[6]...[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]...[15]  Write data
OUTDATA[16]...[x]  not used

## Slide 117: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words

## Slide 118: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 10: Enhanced Write Words

## Slide 119: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 11: Quit
Cancellation of active Enhanced commands
Start by positive edge on I_b_Quit
Start execution Quit:
I_b_Quit:= True  If the signal changes, a Quit command is executed and the active read command is canceled
Quit executed:
O_b_Done = True  Quit command completed
O_B_Status = 16#00

## Slide 120: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 11: Quit
Output data field: Quit command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#02 = Quit command
OUTDATA[3]...[x]  not used

## Slide 121: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 11: Quit

## Slide 122: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed :
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 123: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB Head1Data.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BE = Command Read Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#55 = U = System U
Byte[4]...[5]  Parameter code; 16#5054 = PT = Transmit power
Byte[6]...[7]  Parameter length

## Slide 124: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 125: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
Transmission power read out
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  PT1; 16#0032 = 50mW
ReadData[2] ...[3]  PT2; optional
ReadData[4] ...[5]  PT3; optional
ReadData[6] ...[7]  PT4; optional
ReadData[8] ...[9]  PT5; optional
ReadData[10] ...[11]  PT6; optional
ReadData[12] ...[13]  PT7; optional
ReadData[14] ...[15]  PT8; optional
ReadData[16] ...[17]  PT9; optional
ReadData[18] ...[19]  PT10; optional

## Slide 126: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
Input data field: Transmission power read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BE = Read parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]...[7]  Length parameter; 16#0002 = 2 bytes
INDATA[8]...[9]  Transmission power; 16#0032 = 50mW
INDATA[10]...[x]  not used

## Slide 127: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power
Output data field: Read parameter command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BE = Read Parameter
OUTDATA[3]...[4]  not used
OUTDATA[5]  System Code; 16#55 = "U" = System U
OUTDATA[6]...[7]  Parameter code; 16#5054 = PT = Transmit power
OUTDATA[8]...[9]  Parameter length

## Slide 128: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 12: Special Command  Read out transmission power

## Slide 129: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed:
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 130: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB Head1Data.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BF = Command Write Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#55 = U = System U
Byte[4]...[5]  Parameter code; 16#5244 = RD = Reset to Default
Byte[6]...[7]  Parameter length
Byte[8]...[x]  Parameter data

## Slide 131: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 132: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1
Input data field: Reset to factory setting executed
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BF = Write parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]...[x]  not used

## Slide 133: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1
Output data field: Write Parameter command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BF = Write parameter
OUTDATA[3]...[4]  not used
OUTDATA[5]  System Code; 16#55 = "U" = System U
OUTDATA[6]...[7]  Parameter identifier; 16#5244 = RD = Reset to Default
OUTDATA[8]...[9]  Parameter length
OUTDATA[10]...[x]  Parameter data

## Slide 134: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 13: Special Command  Reset to factory setting IUH-F19x-V1

## Slide 135: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 14: Read out UHF Parameter IUH-F19x-V1
Read access to all UHF parameters of the IUH-F19x-V1
Automatic read access to all parameters one after the other
Start read operation UHF Parameter:
I_b_WriteParameter = False
IO_b_StartConfig = True
End read operation:
O_b_EndConfig = True

## Slide 136: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 14: Read out UHF Parameter IUH-F19x-V1

## Slide 137: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 14: Read out UHF Parameter IUH-F19x-V1

## Slide 138: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 15: Change UHF Parameter IUH-F19x-V1
Write access to changeable UHF parameters IUH-F19x-V1
Parameter values are preset with the factory setting
Start write operation UHF Parameter:
I_b_WriteParameter = True
IO_b_StartConfig = True
End write operation:
O_b_EndConfig = True

## Slide 139: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 15: Change UHF Parameter IUH-F19x-V1

## Slide 140: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Example 15: Change UHF Parameter IUH-F19x-V1

## Slide 141: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter IF – additional information
Activate to send a further information telegram (status 16#0B) including the RSSI value
The further information are inside the data structure Head1/2Data.TagInformation
This telegram will send directly after a status 16#00 telegram which include the read in information
Only support of this function if MultiFrame protocol (parameter QV = “M”) is activated
Deactivated = 16#00; Activated = 16#01
Default setting: 16#00
Switch on parameter IF
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#49 ‘I’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#01 (Parame value)
Read out parameter IF
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#49 ‘I’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 142: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter AP – antenna polarization
Defines the polarization plane of the antenna
In “Combined Mode” (C) the head tries to access the tag with a horizontal and a vertical polarization plane
A switch to a horizontal (H) or a vertical (V) polarization plane is possible
Use “Combined Mode” if the tag orientation is unknown or different
Use horizontal or vertical if the tag orientation is always the same
Define Combined Mode (Default setting) Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#41 ‘A’ (Parameter Code)
Byte[5]  16#50 ‘P’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#43 (Parame value)
Read out parameter AP
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#41 ‘A’ (Parameter Code)
Byte[5]  16#50 ‘P’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 143: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter AP – antenna polarization
Polarization Modes:
Combined Mode “C”  horizontal and vertical polarization plane
Vertical “V”  vertical polarization plane (only)
Horizontal “H”  horizontal polarization plane (only)
Orientation polarization planes:
1  vertical polarization plane
2  horizontal polarization plane
Behavior:
If the tag orientation is unknown or randomly  use Combined Mode to execute a tag access with both polarization planes
If the tag orientation is knows and identically  use horizontal or vertical polarization plane
Polarization plane of the head must be identical to the polarization plane of the data carrier (see data sheet of the data carrier)
If only one polarization plane is defined there will not execute tag access tries with the other polarization plane  reduction the number of inventory rounds on the air interface
The execution time of a command reduces by using only one polarization plane

## Slide 144: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter CD – sending channels
Defines the channel numbers and the sequence of the transmission channels of the air interface
Only valid for the devices which use the Dense Reader Mode (depending on the local regulations)
In default setting the channel 4, 10, 7 and 13 are used (FR1-01)
Define Channel 4, 10, 7, 13 (Default setting FR1-01)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#43 ‘C’ (Parameter Code)
Byte[5]  16#44 ‘D’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#04 (Param. Length)
Byte[8]  16#04 (Channel 4)
Byte[9]  16#0A (Channel 10)
Byte[10]  16#07 (Channel 7)
Byte[11]  16#0D (Channel 13)
Read out parameter CD
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#43 ‘C’ (Parameter Code)
Byte[5]  16#44 ‘D’ (Parameter Code Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 145: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter CD – sending channels
Transmission Channels: Setting the number and the order of the transmission channels of the radio interface during an inventory round
The parameter is only supported by the variant IUH-F19x-FR1-01 (Europe). This device uses the Dense Reader Mode (DRM) where only channels 4, 7, 10 and 13 of the channel spectrum can be used. It is possible to change the number and the order of the channels by this parameter.
The following setting for transmission channels is possible:
Channel 4, Channel 10, Channel 7 and Channel 14
It is possible to change the number and the order of the channels.
Default setting is following:
Transmission Channel 1: Channel 4
Transmission Channel 2: Channel 10
Transmission Channel 3: Channel 7
Transmission Channel 4: Channel 13
The number of transmission channels used can be reduced by the "Transmission Channels" (CD) parameter. If fewer transmission channels are used, the execution time for a scan cycle on a power level is reduced. Fewer scans are executed per power level and the ramp function for the output power is faster.
When reducing the number of transmit channels, it is recommended to keep channels 7 and 10, which are located in the middle of the channel spectrum, since data carriers are tuned to the middle frequency of the spectrum.

## Slide 146: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter E5 – enhanced status 5 (tag lost smoothing)
Defines the number of unsuccessful read/write attempts on the radio interface until a status 5 message
“tag leaves detection zone” is generated during execution of an Enhanced command
Default setting: 16#05 (5 reading attempts)
Value range: 16#00….16#FC (252dec)
Switch parameter E5 to 16#05 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#45 ‘E’ (Parameter Code)
Byte[5]  16#35 ‘5’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#05 (Parame value)
Read out parameter E5
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#45 ‘E’ (Parameter Code)
Byte[5]  16#35 ‘5’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 147: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter MB – memory bank
Defines the memory bank which is accessed by the Single/Enhanced Read/Write Words commands
Influence the read/write commands for 2-Byte words (Standard command) and
4-Byte blocks (Special command)
Not relevant for Fixcode and Special Fixcode (UII/EPC) command
Necessary for writing an EPC longer than 12 Byte
Default setting: 16#03 (User Memory bank)
Value range: 16#00 (reserved); 16#01 (UII/EPC); 16#02 (TID); 16#03 (User Memory)
Switch parameter MB to 16#03 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4D ‘M’ (Parameter Code)
Byte[5]  16#42 ‘B’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#03 (Parame value)
Read out parameter MB
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4D ‘M’ (Parameter Code)
Byte[5]  16#42 ‘B’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 148: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter NT – number of tags
Sets the number of data carriers identified during the execution of a Single command before the
command is automatically aborted
Stop criteria of a Single command in combination with a ramp for the output power
Reduction of overreaches
Default setting: 16#FF (switched off)
Value range: 16#00…16#FE; 16#FF
Switch parameter NT to 16#FF (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#FF (Parame value)
Read out parameter NT
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 149: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter QV – protocol mode
Defines the communication protocol of the IUH-F19x-V1 RFID device
MultiFrame (M; 16#4D) allows the access to several tags inside the detection zone
Function block is designed for MultiFrame Protocol
A switch to SingleFrame protocol require another function block
Do not change the parameter configuration; use default setting
Default setting: 16#4D (MultiFrame)
Value range: 16#4D (MultiFrame); 16#53 (SingleFrame)
Switch parameter QV to 16#4D (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#56 ‘V’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#4D (Parame value)
Read out parameter QV
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#56 ‘V’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 150: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter QW – Q value (number time slots)
Defines the number of time slots for the tag communication with 2^QW ( number of time slots)
With an increasing number of data carrier to be identified, the value of QW must be increased to avoid
collisions if several tags response inside the same time slot
The number of time slots should correspond to the number of expected tags in the detection zone
Default setting: 16#02 (4 time slots)
Value range: 16#00 (1 time slot); 16#07 (128 time slots)
Switch parameter QW to 16#02 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#57 ‘W’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#02 (Parame value)
Read out parameter QW
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#57 ‘W’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 151: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter SM – sensing mode (transmission pauses)
Sets a pause time in milliseconds during the execution of an Enhanced command
The pause takes place after the execution of all inventory rounds
Inside the pause the reader is inactive and does not emit an electromagnetic wave
Option to reduce the internal heating and place the reader in a location with higher temperatures
Default setting: 16#0064 (100ms; FR1); 16#0000 (0ms; FR2)
Value range: 16#0064…16#FFFF (100ms…65535ms; FR1); 16#0000…16#FFFF (0ms…65535ms; FR2)
Switch parameter SM to 16#0064 (Default setting FR1)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#4D ‘M’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#02 (Param. Length)
Byte[8]  16#00 (Parame value)
Byte[8]  16#64 (Parame value)
Read out parameter SM
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#4D ‘M’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 152: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter TA – tries allowed
Defines the number of the allowed read and write attempts for the access of a data carrier
By increasing the parameter value you achieve a more reliable reading and writing process but the
response time of the system increase
When executing Enhanced commands an increasing value of TA reduce the number of pause times
Default setting: 16#02
Value range: 16#01…16#FF
Switch parameter TA to 16#02 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#41 ‘A’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#02 (Parame value)
Read out parameter TA
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#41 ‘A’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 153: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter PT – power transmit (output power)
Set the output power in mW of the system
The range of the output power and the default setting depends on the country specific regulations
The configuration of several levels (PT1, PT2 …PT10) for an output power ramp is possible
With the configuration of several power levels the execution time of a command increase
Default setting: PT1 = 16#0032 (50mW; FR1-01); 16#007D (125mW; FR2-02); 16#0050 (80mW; FR2-03)
Value range: 3, 4, 5, 6, 8, 10, 13, 15, 20, 25, 30, 40, 50, 60, 80, 100, 125, 150, 200, 250, 300, 400, 500,
600, 800, 1000, 1250, 1500, 2000, 2500, 3000, 4000 (mW)
Switch parameter PT to 16#0032 (Default setting; FR1-01)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#50 ‘P’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#02 (Param. Length)
Byte[8]  16#00 (Parame value)
Byte[9]  16#32 (Parame value)
Read out parameter PT
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#50 ‘P’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 154: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter MF – measured reflection
This parameter is only readable if the horizontal or the vertical polarization plane is activated
(parameter AP = “H” or “V”)
If the Combined Mode is activated no measurement is possible
The parameter measure the reflected transmission power of the antenna and the environment
The reflection measured for each transmission channel (see parameter CD and NC) and respond
in a Byte for each channel
To obtain the reflected power in dBm subtract 100 from the response value in decimal format
Option to check the influence of the environmental conditions to the performance of the reader
Read out parameter MF
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4D ‘M’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 155: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter RC – region code
Define the region code for the heads IUH-F192-V1-FR
The region code is used to adjust the head to the radio regulations of the country of operation
When using the IUH-F190-V1-FR heads, the region code can only be read out; a change is not possible
Switch parameter RC to 16#0001 (setuo for version FR1-01)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#52 ‘R’ (Parameter Code)
Byte[5]  16#43 ‘C’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#02 (Param. Length)
Byte[8]  16#00 (Parame value)
Byte[9]  16#01 (Parame value)
Read out parameter RC
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#52 ‘R’ (Parameter Code)
Byte[5]  16#43 ‘C’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 156: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter NC – number channels
Defines the number of Channels on which a read or write attempt is performed during an inventory cycle
For devices which use the “frequency hopping spread spectrum” as access method the parameter is
readable and writable (Region code: 2, 3, 7, 9, 10, 11, 12, 13, 14)
For devices which use the “parameterizable frequency list” as access method the parameter is
readable only (Region code: 1, 4, 5, 6, 8)
Switch parameter NC to 16#32 (setuo for version FR2-02)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#43 ‘C’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#32 (Parame value)
Read out parameter NC
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#43 ‘C’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 157: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter FL – filter list
This parameter is only readable and contain the current configuration of the filter mask
There are 3 filter mask available (mask 0, 1 and 2)
The filter mask must be set using the FI command (via Special command)
Read out parameter Filter Mask 0
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#4C ‘L’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 158: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter SE – session
This parameter is only for Service! Do not change it !!!
Session 0: 16#00; Session 1: 16#01; Session 2: 16#02; Session 3: 16#03
Default: 16#01 (Session 1)
Switch parameter SE to 16#02
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#45 ‘E’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#02 (Parame value)
Read out parameter SE
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#45 ‘E’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 159: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter FB – search mode
This parameter is only for Service! Do not change it !!!
Defines the Search Mode of the head
Default: 16#00
MultiTag applications: 16#01
Switch parameter FB to 16#01
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#42 ‘B’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#01 (Parame value)
Read out parameter FB
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#42 ‘B’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 160: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter FR – first read
This parameter is only for Service! Do not change it !!!
Defines the behavior of the write process
Default: 16#00 (defined by TagType)
16#01: Read before write
16#02: Write
Switch parameter FR to 16#00 (default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter FR
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 161: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Parameter EF – fixcode length
This parameter is only for Service! Do not change it !!!
Used for command Read Fixcode
Default: 16#00 (automatic)
Read out parameter EF
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#55 ‘U’ (System Code)
Byte[4]  16#45 ‘E’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 162: Contact
Karsten Reinhardt
kreinhardt@de.pepperl-fuchs.com
+49 (0) 621 776 1736

## Slide 163: IC-KP2-2HB21 + IUH-F19x-V1 MF TwinCAT 3
Version history:
V1.0 21.01.2025
Initial version