## Slide 2: Commissioning function block IC-KP2-2HB21-2V1D + IQH3-FP-V1
TwinCAT 3 function block for the evaluation unit
IC-KP2-2HB21-2V1D (EtherCAT) with SingleFrame protocol for connecting the IQH3-FP-V1 RFID device

## Slide 3: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
This documentation is valid with the following specification:
Beckhoff PLC and TwinCAT 3 programming environment
Single frame protocol
Valid for the IQ system (13.56MHz) for connection of the IQH3-FP-V1 head with configuration protocol mode QV "SingleFrame"
IDENTControl IC-KP2-2HB21-2V1D (EtherCAT)

## Slide 4: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Content Download:
Version history
Documentation (DEU, ENG)

## Slide 5: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Content:
Scanning for connected devices
Link process data field input data
Link process data field output data
Change EtherCAT telegram length
Read Firmware Version
Configuration of proces data fields
Inputs and Outputs function block
Declaration of function and data block
Structure of data block IDENTControl_UserData
Schematic representation of the function and data blocks
Example 1: Initialization
Example 2: Single Read Fixcode (UID) one-time read access to the Fixcode (UID)
Example 3: Single Read Words one-time read access to the User Memory
Example 4: Single Write Words one-time write access to the User Memory
Example 5: Enhanced Read Fixcode (UID) permanent read access to the Fixcode (UID)
Example 6: Enhanced Read Words permanent read access to the User Memory
Example 7: Enhanced Write Words permanent write access to the User Memory
Example 8: Quit stop of an Enhanced command
Example 9: Special Command  Read out transmission power execution of a freely defined command
Example 10: Special Command  Reset to factory status of IQH3-FP-V1 execution of a freely defined command
Example 11: Read out HF Parameter IQH3-FP-V1 read access to HF Parameter
Example 12: Change HF Parameter IQH3-FP-V1 write access to HF Parameter
Parameter IF - additional information Parameter AF - AFI to request Parameter E5 - Enhanced Status 5 Parameter NT - Number of Tags
Parameter QV - Protocol Mode Parameter QW - Definition of time slots Parameter TA - Tries allowed Parameter PT - Power transmit
Parameter DR - Data rate Parameter TI - Tag ID filtering Parameter TO - Overtemperature handling Parameter CT - Tag Type
Parameter OH - Operating time Parameter TE – Temperatures Parameter VO – Voltages Parameter FR - Sequence Mode
Parameter RV - Revision GIT Parameter SN - Serial Number of uC Parameter MM - Multiplex Mode Parameter ST - Status frontend

## Slide 6: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Scanning for connected devices
Activate Config Mode
Right-click on "Device 5 (EtherCAT)“  Scan  IDENTControl with the telegram length set in the device appears

## Slide 7: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Link process data field input data
Activate Config Mode
Right-click on "IN_CH1  Change link activate Array Mode  GVL_IDENTControl.BUS_INPUT[1]  Link from Byte 0 to Byte 63

## Slide 8: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Link process data field output data
Activate Config Mode
Right-click on "OUT_CH1  Change link  activate Array Mode  GVL_IDENTControl.BUS_OUTPUT[1]  Link from Byte 0 to Byte 63

## Slide 9: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Change EtherCAT telegram length
Activate Config Mode  Scan to detect connected device  Double-click on the "IDENTControl Compact 64 Byte IN/OUT" module  EtherCAT  Advanced settings

## Slide 10: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Change EtherCAT telegram length
ESC Access  EEPROM  Smart View  Write EEPROM  select new module size

## Slide 11: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Change EtherCAT telegram length
Remove module  Scan  Read in module with new telegram size  Link process data fields

## Slide 12: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Read Firmware Version
Double-click on IDENTControl Compact module  CoE - Online

## Slide 13: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Configuration of process data fields
Definition as global variables (GVL)
BUS_OUTPUT = Output data field
BUS_INPUT = Input data field
Multidimensional array with a length of 254 bytes

## Slide 14: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Inputs and outputs function block:

## Slide 15: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Inputs and outputs function block:
Name | Typ | Meaning
pADR_IN | PVOID | Address Input data field
cbSIZE_IN | UDINT | Length Input data field
pADR_OUT | PVOID | Address Output data field
cbSIZE_OUT | UDINT | Length Output data field
I_T_Timeout | TIME | Timer for monitoring communication
I_b_StartRead | BOOL | TRUE (positive edge) = Start execution of read command
I_b_StartWrite | BOOL | TRUE (positive edge) = Start execution of write command
I_b_StartSpecialCommand | BOOL | TRUE (positive edge) = Start execution of special command (freely definable command)
I_b_UserMemory_UID | BOOL | FALSE = Access to user data area (user memory) TRUE = Access to Fixcode (UID)
I_b_EPC | BOOL | FALSE = no meaning; specified by I_b_UserMemory_UID TRUE = Access to EPC/UII area (UHF only)

## Slide 16: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Inputs and outputs function block:
Name | Typ | Bedeutung
I_b_SingleEnhanced | Bool | FALSE = Execution Single command (one-time execution) TRUE = Execution Enhanced command (permanent execution)
I_b_Quit | Bool | TRUE (positive edge) = Start execution of Quit command; abort of running Enhanced command
I_w_StartAddress | Word | Start address on data carrier
I_i_WordNumber | Integer | Number of addressed data blocks of 4 bytes each
I_w_TagType | Word | Data carrier type
I_b_WriteParameter | Bool | FALSE = Command is still active or not yet completed; data carrier outside detection zone TRUE = Command completed; data carrier within detection zone (Enhanced)
O_b_Done | Bool | FALSE = Data carrier within detection zone (Enhanced) TRUE = Data carrier outside detection zone (Single and Enhanced)
O_b_NoDataCarrier | Bool | FALSE = Execution Single command (one-time execution) TRUE = Execution Enhanced command (permanent execution)

## Slide 17: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Inputs and outputs function block:
Name | Typ | Bedeutung
O_b_Busy | Bool | FALSE = no command active; negative edge = command ended TRUE = Command active or currently being executed
O_b_Finish | Bool | FALSE = Command is still active or not yet completed; TRUE = command completed
O_b_Error | Bool | FALSE = no error status TRUE = error status; error status on O_B_Status
O_B_Status | Byte | Status value of the command execution
O_B_ReplyCounter | Byte | Response counter
O_b_EndConfig | Bool | TRUE = Parameter access finished
IO_b_SetRestart | Bool | TRUE (positive edge) = Start execution of initialization routine; set input back to False after one cycle
IO_b_InitFinish | Bool | TRUE = Initialization completed successfully; function module ready for operation
IO_b_StartConfig | Bool | TRUE = Start parameter access
UserDataGlobal | Data block | Data block for read and write data

## Slide 18: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Declaration of function and data block
IC_KP2_2HB21_IQH3_SF_Head1  Function block for channel 1 (Type IC_KP2_2HB21_IQH3_SF)
IC_KP2_2HB21_IQH3_SF_Head2  Function block for channel 2 (Type IC_KP2_2HB21_IQH3_SF)
Head1Data  Data block for channel 1 (Type IDENTControl_UserData)
Head2Data  Data block for channel 2 (Type IDENTControl_UserData)

## Slide 19: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Structure of data block IDENTControl_UserData
DUT IDENTControl_UserData
ReadData  contains read in data
WriteData  contains write data
SpecialCommand  Data field for the freely definable command
ReadParam_XX  current parameter value; WriteParam_XX  new parameter value

## Slide 20: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Schematic representation of the function and data blocks:
Function block
IC_KP2_2HB21_IQH3_SF_Head1
Data block
Head1Data
Data block
Head2Data
Note:
Function blocks IC_KP2_2HB21_IQH3_SF_Head1 and IC_KP2_2HB21_IQH3_SF_Head2 from type IC_KP2_2HB21_IQH3_SF
Data blocks
Head1Data and Head2Data from type IDENTControl_UserData
Function block
IDENTControl_FB_SF
UserDataGlobal
Function block
IC_KP2_2HB21_IQH3_SF_Head2
Function block
IDENTControl_FB_SF
UserDataGlobal

## Slide 21: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization
Initialization must be carried out after device start-up
Assignment of the data carrier type to the I_w_TagType input (e.g. IQC21  16#3231 or factory setting  16#3939)
Start by positive edge on IO_b_SetRestart
Initialization successfully completed if signal change at IO_b_InitFinish to True
Before executing a new initialization, IO_b_SetRestart must be reset to False
All variables of the FB are reset; data blocks are overwritten with 16#00
All active Enhanced commands are canceled
Option for error acknowledgement

## Slide 22: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID device | Commands
IQC20 | Alle ISO15693 Datenträger | 16#3230 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode
IQC21 | NXP ICode SLI | 16#3231 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC22 | Texas Instruments Tag-It HF-I Plus | 16#3232 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC24 | Infineon my-D SRF55V10P | 16#3234 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC33 | Fujitsu MB89R118 | 16#3333 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)

## Slide 23: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization
P+F Name | Chip Name | Tag Type | RFID device | Commands
IQC35 | NXP Icode SLI-S | 16#3335 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)
IQC37 | Fujitsu MB89R112 | 16#3337 | IQH1-…-V1; IQH3-FP-V1 (13,56MHz; ISO15693) | Single / Enhanced Read Fixcode Single / Enhanced Read Words Single / Enhanced Write Words Single / Enhanced Write Words with Lock (SpecialCommand)

## Slide 24: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization
Initialization routine:
Start via positive edge on IO_b_SetRestart
Reset input IO_b_SetRestart after at least one cycle
Initialization completed when IO_b_InitFinish = True (positive edge)
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the data carrier type was parameterized incorrectly
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 25: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#04 = Change Tag command
OUTDATA[3]  not used
OUTDATA[4]..[5]  TagType;, 16#3939 = Default setting
OUTDATA[6]….[x]  not used
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#04 = Change Tag command
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 26: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 1: Initialization

## Slide 27: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Single read attempt on the Fixcode (UID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := False
Start by positive edge on I_b_StartRead
Command ends after one read attempt
Read successful, Fixcode read; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := True (access to UID)
I_b_EPC := False (not relevant)
I_b_StartRead := True (start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read not successful, data carrier not recognized and Fixcode not read in:
I_b_SingleEnhanced := False
I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 28: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Data carrier recognized and Fixcode read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 29: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Data carrier recognized and Fixcode read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[7]  Fixcode (8 byte Fixcode; ISO15693)
ReadData[8]...[x]  16#00
The length of the Fixcode depends on the data carrier. All ISO15693 (13.56MHz) data carriers have a Fixcode with a length of 8 bytes.

## Slide 30: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Input data field: Fixcode read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[15]  Fixcode (UID; ISO15693 data carrier)
INDATA[16]…[x]  not used

## Slide 31: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 32: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)
Output data field: Command Single Read Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#01 = Single Read Fixcode
INDATA[3]…[x]  not used

## Slide 33: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)

## Slide 34: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 2: Single Read Fixcode (UID)

## Slide 35: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Single read attempt on the user data area (User Memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start by positive edge on I_b_StartRead
Command ends after one read attempt
Read successful, data read in; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartRead := True (start read process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read not successful, data carrier not recognized and data not read in
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 36: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Data carrier recognized and user data read in:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 37: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Data carrier recognized and user data read:
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[7]  Read data (2 blocks of 4 bytes each)
ReadData[8]...[x]  16#00
The number of blocks to be read in with a block size of 4 bytes each is defined via the input I_i_WordNumber
Note:
When using the IQC33, the I_i_WordNumber must always be a multiple of 2. This data carrier has a block size of 8 bytes.

## Slide 38: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Input data field: User data read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#10 = Single Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Number of transmitted data blocks of 4 bytes each (I_i_WordNumber)
INDATA[8]…[15]  User data read in
INDATA[16]…[x]  not used

## Slide 39: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#10 = Single Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 40: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words
Output data field: Command Single Read Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#10 = Single Read Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of data blocks (I_i_WordNumber)

## Slide 41: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words

## Slide 42: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 3: Single Read Words

## Slide 43: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Single write attempt to the user data area (User Memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := False
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Specify write data in WriteData
Start by positive edge on I_b_StartWrite
Write successful, data written; command completed:
I_b_SingleEnhanced := False (one-time command)
I_b_UserMemory_UID := False (access to User Memory)
I_b_EPC := False (not relevant)
I_b_StartWrite := True (start write process with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write not successful, data carrier not recognized and data not written
I_b_SingleEnhanced := False
I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 44: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB Head1Data.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 45: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Data carrier recognized and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = True
O_b_NoDataCarrier = True
O_b_Busy = False
O_b_Finish = True
O_B_Status = 16#05

## Slide 46: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Input data field: User data written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#40 = Single Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 47: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#40 = Single Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 48: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words
Output data field: Command Single Write Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#40 = Single Write Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]…[15]  Write data
OUTDATA[16]…[x]  not used

## Slide 49: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words

## Slide 50: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 4: Single Write Words

## Slide 51: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Permanent read operation on the Fixcode (UID) of a data carrier
I_b_UserMemory_UID := True and I_b_EPC := False and I_b_SingleEnhanced := True
Start by positive edge on I_b_StartRead
End of command execution via Quit command or initialization
Start read process; read process activated; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Read process activated; data carrier enters detection zone; Fixcode read:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process; read process activated; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := True
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel read process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 52: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Data carrier recognized and Fixcode read; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier detected; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 53: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Data carrier recognized and Fixcode read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[7]  Fixcode (8 byte Fixcode; ISO15693)
ReadData[8]...[x]  16#00
The length of the Fixcode depends on the data carrier. All ISO15693 (13.56MHz) data carriers have a Fixcode with a length of 8 bytes.

## Slide 54: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Input data field: Fixcode read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  not used
INDATA[8]…[15]  Fixcode (UID; ISO15693 data carrier)
INDATA[16]…[x]  not used

## Slide 55: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Input data field: no data carrier detected or data carrier has left the detection zone
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier detected or data carrier has left detection zone
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 56: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)
Output data field: Command Enhanced Read Fixcode
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1D = Enhanced Read Fixcode
INDATA[3]…[x]  not used

## Slide 57: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)

## Slide 58: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 5: Enhanced Read Fixcode (UID)

## Slide 59: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Permanent read operation on the user data area (user memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Start I_b_StartRead; End via Quit command or initialization
Start read process; read process activated; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Read process activated; data carrier enters detection zone; data read:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start read process; read process activated; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartRead := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Abort read process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Read process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 60: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Data carrier recognized and data read in; command active:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier detected; command active:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 61: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Data carrier recognized and user data read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[7]  Read data (2 blocks of 4 bytes each)
ReadData[8]...[x]  16#00
The number of blocks to be read in with a block size of 4 bytes each is defined via the input I_i_WordNumber
Note:
When using the IQC33, the I_i_WordNumber must always be a multiple of 2. This data carrier has a block size of 8 bytes.

## Slide 62: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Input data field: User data read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#19 = Enhanced Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Number of transmitted data blocks of 4 bytes each (I_i_WordNumber)
INDATA[8]…[15]  User data read in
INDATA[16]…[x]  not used

## Slide 63: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#19 = Enhanced Read Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 64: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words
Output data field: Command Enhanced Read Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#19 = Enhanced Read Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of data blocks (I_i_WordNumber)

## Slide 65: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words

## Slide 66: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 6: Enhanced Read Words

## Slide 67: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Permanent write operation to the user data area (user memory) of a data carrier
I_b_UserMemory_UID := False and I_b_EPC := False and I_b_SingleEnhanced := True
I_w_StartAddress := 16#0000 (variable) and I_i_WordNumber := 2 (variable)
Write data WriteData; start via I_b_StartWrite; end via Quit command
Start write process; write process active; no data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False
Write process activated; data carrier enters detection zone; data written:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Start write process; write process active; data carrier in the detection zone:
I_b_SingleEnhanced := True I_b_UserMemory_UID := False
I_b_EPC := False
I_b_StartWrite := True
O_b_Busy = True
O_b_Done = True
O_b_Finish = False
O_b_NoDataCarrier = False
O_b_Error = False
Cancel write process via Quit
I_b_Quit := True
O_b_Busy = False
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False
Write process active; data carrier leaves detection zone
O_b_Busy = True
O_b_Done = False
O_b_Finish = False
O_b_NoDataCarrier = True
O_b_Error = False

## Slide 68: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Write data:
Assignment before the start of command execution
Assignment within the DB Head1Data.WriteData.WriteData[x]
Byte[0] to [x]  Write data
Number of write data depending on parameter I_i_NumberWords and the telegram length

## Slide 69: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Data carrier recognized and user data written:
O_b_Done = True
O_b_NoDataCarrier = False
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#00
No data carrier recognized:
O_b_Done = False
O_b_NoDataCarrier = True
O_b_Busy = True
O_b_Finish = False
O_B_Status = 16#05

## Slide 70: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Input data field: User data written
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1A = Enhanced Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 71: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Input data field: no data carrier recognized
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#1A = Enhanced Write Words
INDATA[3]  not used
INDATA[4]  Status; 16#05 = no data carrier recognized
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 72: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words
Output data field: Command Enhanced Write Words
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#1A = Enhanced Write Words
OUTDATA[3]  not used
OUTDATA[4]…[5]  Start address (I_w_StartAddress)
OUTDATA[6]…[7]  Number of blocks (I_i_WordNumber)
OUTDATA[8]…[15]  Write data
OUTDATA[16]…[x]  not used

## Slide 73: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words

## Slide 74: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 7: Enhanced Write Words

## Slide 75: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 8: Quit
Cancellation of active Enhanced commands
Start by positive edge on I_b_Quit
Start execution Quit:
I_b_Quit:= True  If the signal changes, a Quit command is executed and the active read command is canceled
Quit executed:
O_b_Done = True  Quit command completed
O_B_Status = 16#00

## Slide 76: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 8: Quit
Input data field: Quit command executed
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#02 = Quit command
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 77: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 8: Quit
Output data field: Quit command
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#02 = Quit command
OUTDATA[3]…[x]  not used

## Slide 78: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 8: Quit

## Slide 79: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed:
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 80: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB UserData.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BE = Command Read Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#51 = Q = System Q
Byte[4]...[5]  Parameter code; 16#5054 = PT = Transmit power
Byte[6]...[7]  Parameter length

## Slide 81: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 82: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
Transmission power read
DB Head1Data.ReadData.ReadData[x]
ReadData[0] ...[1]  16#0004 = Maximum

## Slide 83: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
Input data field: transmission power read in
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BE = Read Parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[7]  Length parameter; 16#0002 = 2 Byte
INDATA[8]…[9]  transmission power; 16#0004 = Maximum
INDATA[10]…[x]  not used

## Slide 84: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power
Output data field: Command Read Parameter
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BE = Read Parameter
OUTDATA[3]…[4]  not used
OUTDATA[5]  System Code; 16#51 = „Q“ = System Q
OUTDATA[6]…[7]  Parameter sign; 16#5054 = PT = transmission power
OUTDATA[8]…[9]  Length Parameter

## Slide 85: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 9: Special Command  Read out transmission power

## Slide 86: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1
All commands that cannot be parameterized via the input parameters of the function block can be executed
All commands supported by the evaluation unit can be executed
Parameterization Command telegram in the SpecialCommand data field
Start by positive edge on I_b_StartSpecialCommand
Start SpecialCommand and successfully completed:
I_b_SingleEnhanced := False (not relevant)
I_b_UserMemory_UID := False (not relevant)
I_b_EPC := False (not relevant)
I_b_StartSpecialCommand := True (Start command transmission with positive edge)
O_b_Busy = False (no command active)
O_b_Done = True
O_b_Finish = True
O_b_NoDataCarrier = False
O_b_Error = False

## Slide 87: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1
Configuration of freely definable command:
Assignment before the start of command execution in the SpecialCommand data field
Assignment within the DB Head1Data.SpecialCommand.SpecialCommand[x]
Byte[0]  Command code; 16#BF = Command Write Parameter
Byte[1]...[2]  not used
Byte[3]  System Code; 16#51 = Q = System Q
Byte[4]…[5]  Parameter code; 16#5244 = RD = Reset to Default
Byte[6]…[7]  Parameter length
Byte[8]…[x]  Parameter data

## Slide 88: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1
SpecialCommand:
Start via positive edge on IO_b_StartSpecialCommand
Reset input IO_b_StartSpecialCommand after at least one cycle
O_b_Done = True
O_b_Finish = True
O_B_Status = 16#00
O_B_ReplyCounter was increased
If the status contains a value 16#04 (parameter error), the command is incorrectly parameterized
If the status contains a value 16#06 (no head), no RFID head is connected to this channel

## Slide 89: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1
Input data field: reset to factory status executed
INDATA.INDATA[x]
Input data field:
INDATA[0]  Control Byte
INDATA[1]  not used
INDATA[2]  Command code; 16#BF = Write Parameter
INDATA[3]  not used
INDATA[4]  Status; 16#00 = ok
INDATA[5]  Reply Counter
INDATA[6]…[x]  not used

## Slide 90: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1
Output data field: Command Write Parameter
OUTDATA.OUTDATA[x]
Output data field:
OUTDATA[0]  Control Byte
OUTDATA[1]  not used
OUTDATA[2]  Command code; 16#BF = Write Parameter
OUTDATA[3]…[4]  not used
OUTDATA[5]  System Code; 16#51 = „Q“ = System Q
OUTDATA[6]…[7]  Parameter sign; 16#5244 = RD = Reset to Default
OUTDATA[8]…[9]  Length Parameter
OUTDATA[10]…[x]  Parameter data

## Slide 91: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 10: Special Command  Reset to factory status of IQH3-FP-V1

## Slide 92: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 11: Read out HF Parameter IQH3-FP-V1
Read access to all HF parameters of the IQH3-FP-V1
Automatic read access to all parameters one after the other
Start read access HF Parameter:
I_b_WriteParameter = False
IO_b_StartConfig = True
End of read access:
O_b_EndConfig = True

## Slide 93: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 11: Read out HF Parameter IQH3-FP-V1

## Slide 94: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 11: Read out HF Parameter IQH3-FP-V1

## Slide 95: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 11: Read out HF Parameter IQH3-FP-V1

## Slide 96: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 12: Change HF Parameter IQH3-FP-V1
Write access to changeable HF parameters IQH3-FP-V1
Parameter values are pre-assigned with the factory setting
Start write access HF Parameter:
I_b_WriteParameter = True
IO_b_StartConfig = True
End of write access:
O_b_EndConfig = True

## Slide 97: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Example 12: Change HF Parameter IQH3-FP-V1

## Slide 98: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter IF – additional information:
Activate to send a further information telegram (status 16#0B) including the RSSI value
of the tag response
This telegram will send directly after a status 16#00 which include the read in information
Only support of this function if MultiFrame protocol (parameter QV = “M”) is activated
Using SingleFrame protocol can not transmit the telegram with the further information
also if the parameter is activated
Deactivated = 16#00; Activated = 16#01
Default setting: 16#00
Switch off parameter IF (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#49 ‘I’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter IF
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#49 ‘I’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 99: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter AF – AFI to request:
Defines a filter that only a tag response which does have the same value inside the AFI Byte
Value inside the AFI Byte need to preconfigure with the commands SC and EC before
Use default configuration and do not change parameter
Default setting: 16#00 (all tags will transmit)
Value range: 16#00….16#FF
Switch parameter AF to 16#00 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#41 ‘A’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter AF
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#41 ‘A’ (Parameter Code)
Byte[5]  16#46 ‘F’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 100: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter E5 – Enhanced status 5 (tag lost smoothing):
Defines the number of unsuccessful read/write attempts on the air interface until a status 5
message “tag leaves detection zone” is generated
Default setting: 16#05 (5 reading attempts)
Value range: 16#00….16#0A (10dec)
Switch parameter E5 to 16#05 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#45 ‘E’ (Parameter Code)
Byte[5]  16#35 ‘5’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#05 (Parame value)
Read out parameter E5
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#45 ‘E’ (Parameter Code)
Byte[5]  16#35 ‘5’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 101: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter NT – Number of tags to find:
Sets the number of data carriers identified during the execution of a Single command before
the command is automatically aborted
Only valid if the MultiFrame protocol is activated; no relevance for SingleFrame protocol
Default setting: 16#FF (no stop of the command)
Value range: 16#01….16#14; 16#FF
Switch parameter NT to 16#FF (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#05 (Parame value)
Read out parameter NT
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#4E ‘N’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 102: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter QV – Protocol Mode:
Defines the communication protocol of the IQH3-FP-V1 RFID device
SingleFrame (S; 16#53; default) is the compatible protocol for the existing
system IQ (IQH1-…-V1)
MultiFrame (M; 16#4D) allows the access to several tags inside the detection zone
Function block is designed for SingleFrame Protocol
A switch to MultiFrame protocol require another function block
Do not change the parameter configuration; use default setting
Switch parameter QV to “S” (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#56 ‘V’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#53 ‘Q’ (Parame value)
Read out parameter QV
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#56 ‘V’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 103: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter QW – Definition of used slots:
Defines the used time slots on the air interface which are used for the tag communication
Only relevant for application with several tags inside the detection zone
at the same time (MultiFrame)
0 (16#00) = single tag; 1 (16#01) = dual tag; 2 (16#02) = multi tag;
3 (16#03) = very many tag; 4 (16#04) = very very many tags
Parameter range: 0…4 (16#00….16#04)
Default setting: 0 (16#00)
Do not change parameter; use default setting
Switch parameter QW to 16#00 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#57 ‘W’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter QW
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#51 ‘Q’ (Parameter Code)
Byte[5]  16#57 ‘W’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 104: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter TA – Tries allowed:
Defines the number of the allowed read and write attempts for the access of a data carrier
By increasing the parameter value you achieve a more reliable reading and
writing process but the response time of the system increase
Parameter range: 1…10
Default value: 2
Switch parameter TA to 16#02 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#41 ‘A’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#02 (Parame value)
Read out parameter TA
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#41 ‘A’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 105: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter PT – Power transmit (output power):
Set the output power of the system and influence the detection range
Min = 1 (16#0001); Eco = 2 (16#0002); Normal = 3 (16#0003); Power = 4 (16#0004)
Parameter range: 1…4 (16#0001….16#0004)
Default value: 4 (16#0004)
Switch parameter PT to 16#0004 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#50 ‘P’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#02 (Param. Length)
Byte[8]  16#00 (Parame value)
Byte[9]  16#04 (Parame value)
Read out parameter PT
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#50 ‘P’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 106: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter DR – Data rate for read:
Set the data rate (transmission rate) for the read access of ISO15693-2 X2 tags
Valid for IQC21/33/34/37/39/50 tags for the read access of more than 2 data blocks
Increase the reading speed but also the susceptibility to interferences
Parameter range: 0 (16#00)…1 (16#01);
0 = normal; 1 = fast read mode
Default value: 0 (16#00)
Switch parameter DR to 16#00 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#44 ‘D’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter DR
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#44 ‘D’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 107: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter TI – Tag ID filtering on UID:
Set the first part of the UID for filtering on it
Possible to define a specific UID or a leading part of the UID
Configuration of the length of the UID necessary
Switch parameter TI to 16#00 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#49 ‘I’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter TI
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#49 ‘I’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)
Structure parameter TI
TI[0]  Length parameter high Byte
TI[1]  Length parameter high Byte
TI[2]  UID Byte 1 (16#E0)
TI[3]  UID Byte 2 (16#xx)
TI[4]  UID Byte 3 (16#xx)
TI[5]  UID Byte 4 (16#xx)
TI[6]  UID Byte 5 (16#xx)
TI[7]  UID Byte 6 (16#xx)

## Slide 108: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter TO – Over temperature handling:
Define the behavior of the system if there is an overtemperature situation
Parameter range: 0…2 (0 = Switched off; 1 = reduce power; 2 = reduce duty cycle)
Default value: 0
Switch parameter TO to 16#00 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#4F ‘O’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#00 (Parame value)
Read out parameter TO
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#4F ‘O’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 109: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter CT – Tag Type:
Read out the actual configured Tag Type
Only read access implemented
Tag Type is configured by the command “Change Tag”
Parameter range: 20…50 (dec)
Default value: 20 (auto detect)
Read out parameter CT
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#43 ‘C’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 110: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter OH – operating time:
Read out operating time in hours for system uptime and carrier uptime
32 bit unsigned value for both time values
Read out parameter OH
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#4F ‘O’ (Parameter Code)
Byte[5]  16#48 ‘H’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)
Structure parameter OH
OH[0]  Operating time device in hours
OH[1]  time of active radio interface in hours
OH[2]  Operating time device in days
OH[3]  time of active radio interface in days
OH[4]  Operating time device in weeks
OH[5]  time of active radio interface in weeks

## Slide 111: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter TE – Temperatures:
Read out actual temperatures in °C for PA and uC
8 bit signed value for both temperature values
Read out parameter TE
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#54 ‘T’ (Parameter Code)
Byte[5]  16#45 ‘E’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)
Structure parameter TE
TE[0]  Temperature in °C at power amplifier
TE[1]  Temperature in °C at u controller

## Slide 112: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter VO – Voltages and currents:
Read out actual voltages and currents
Voltages in mV and currents in mA
16 bit unsigned value for all values
Read out parameter VO
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#56 ‘V’ (Parameter Code)
Byte[5]  16#4F ‘O’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 113: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter FR – sequence mode:
Define the command sequence if a write command is executed
Parameter range: 1…3 (1 = write after read; 2 = always write; 3 = read after write after read)
Default value: 1
Read out parameter FR
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)
Switch parameter FR to 16#01 (Default setting)
Byte[0]  16#BF (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#46 ‘F’ (Parameter Code)
Byte[5]  16#52 ‘R’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#01 (Param. Length)
Byte[8]  16#01 (Parame value)

## Slide 114: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter RV – Revision GIT:
Read out the revision of the GIT
Read out parameter RV
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#52 ‘R’ (Parameter Code)
Byte[5]  16#56 ‘V’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 115: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter SN – Serial number of uC:
Read out the serial number of the internal uC STM32
Read out parameter SN
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#4E ‘N’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 116: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter MM – Multiplex Mode:
Read out the status of the Multiplex Mode configuration
Only read access to this parameter
Multiplex Mode need to be activated by the command “MM” over the IDENTControl unit
Necessary if active heads close to each other
Time multiplexing of several heads
Read out parameter MM
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#4D ‘M’ (Parameter Code)
Byte[5]  16#4D ‘M’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 117: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Parameter ST – Status of front end:
Read out the status of the front end
Only read access to this parameter
Shows the actual status and the latched status
Read out parameter ST
Byte[0]  16#BE (command)
Byte[1]  16#00 (not used)
Byte[2]  16#00 (not used)
Byte[3]  16#51 ‘Q’ (System Code)
Byte[4]  16#53 ‘S’ (Parameter Code)
Byte[5]  16#54 ‘T’ (Parameter Code)
Byte[6]  16#00 (Param. Length)
Byte[7]  16#00 (Param. Length)
Byte[8]  16#00 (Parame value)

## Slide 118: Contact
Karsten Reinhardt
kreinhardt@de.pepperl-fuchs.com
+49 (0) 621 776 1736

## Slide 119: IC-KP2-2HB21 + IQH3-FP-V1 SF TwinCAT 3
Version history:
V1.0 10.10.2024
Initiale Version